## Slide 1: CSEN20
Fall 2026
Introduction to Embedded Systems
Michael Schimpf, PhD, mschimpf@scu.edu

## Slide 2: Chapter 2 Binary Number Systems

## Slide 3: Kinds Of Data
Numbers
  Integers
    Unsigned
    Signed
  Reals
    Fixed-Point
    Floating-Point
Text
  ASCII Characters
  Strings
Other
  Graphics
  Images
  Video
  Audio
Depending on interpretation!

## Slide 4: Number Representation
Computers use binary numbers (0's and 1's).
  How many digits (bits) do I need to represent decimal 7 in bin? 1 + 2 + 4 = 7 -> 3 bits

## Slide 5: Number Representation
2. Computers use numbers with fixed number of digits (“fixed-precision”).
Byte
Half-word
Word
Double-word
Why do we need all these data types?

## Slide 6: Number Representation
3. Computers represents:
signed numbers using "2's complement" instead of “sign- and-magnitude” representation. Why?

## Slide 7: Sign-and-Magnitude vs 2’s Complement

## Slide 8: Sign-and-Magnitude Representation
Dec | Binary
+0 | 0000
+1 | 0001
+2 | 0010
+3 | 0011
+4 | 0100
+5 | 0101
+6 | 0110
+7 | 0111
Dec | Binary
-0 | 1000
-1 | 1001
-2 | 1010
-3 | 1011
-4 | 1100
-5 | 1101
-6 | 1110
-7 | 1111
Two 0 representations?!?!?!
if (x == +0 && x == -0){
…
}

## Slide 9: 2’s Complement Representation
Dec | Binary
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
Dec | Binary
-1 | 1111
-2 | 1110
-3 | 1101
-4 | 1100
-5 | 1011
-6 | 1010
-7 | 1001
-8 | 1000
One “–” more

## Slide 10: Why Not Sign + Magnitude?
Complicates addition :
  First check the signs!
    if (same) add both and use the same sign;
    else (!same) subtract the smaller from the larger; use the sign of the larger.
  How do you determine which is smaller/larger?
+210 = 0010
+(-710) = +1111
????
111 > 010:
111
- 010
101
Use sign of 111:
1101
= -510
larger
smaller

## Slide 11: Why 2’s Complement?
Signed:
+210 = 0010
+(-710) = +1001 1011 = -510
Unsigned:
+210 = 0010
+(910) = +1001
1011
=1110
Easy addition/subtractions

## Slide 12: Why Not Sign+Magnitude?
Main reasons:
Two zero representations are very annoying (and a math problem!)
One value is wasted
Hardware implementation is complicated
Addition without check, which operand is larger.
Simply add numbers.
One hardware adder works for both signed and unsigned

## Slide 13: Chapter 2 Binary Number Systems
Part 1: Polynomial Evaluation

## Slide 14: Symbols and their values used in positional number systems
System | Radix | Digit Symbols | Corresponding Digit Values
Binary | 2 | 0,1 | 0,1
Decimal | 10 | 0,1,2,3,4, 5,6,7,8,9 | 0,1,2,3,4, 5,6,7,8,9
Hex | 16 | 0,1,2,3,4,5,6,7, 8,9,A,B,C,D,E,F | 0,1,2,3,4,5,6,7, 8,9,10,11,12,13,14,15

## Slide 15: Positional Number Systems
Numeric values are represented by a sequence of digit symbols.
– Examples: 235410 , 11012, F8ED16
Symbols represent numeric values.
  Symbols are not limited to ‘0’-’9’ additional ‘A’ – ‘F’!
  Example: AFED16

## Slide 16: POLYNOMIAL EVALUATION
Example: 367210
+ +
  where: are the corresponding digit values
  and: is the radix (number base)
  Ex: = 367210
Subscript used to identify radix (R)
These are the digit symbols

## Slide 17: Polynomial Evaluation
Polynomial Evaluation can be used to convert:
A number in any base to base 10 (Base aka Radix)
***Important Note:
  Polynomial evaluation only works when converting to base 10.
  It doesn’t work if you convert it in the other direction I.e., from decimal to something else! In those cases, we use other techniques

## Slide 18: POLYNOMIAL EVALUATION
547
Symbolic representation (What we write)
Numeric interpretation
(What we understand)
Subscript indicate the radix (number base)
Digit values (coefficients)
Positional weights (powers of the radix)
 5×102 + 4×101 + 7×100
= 500 + 40 + 7
= 547
10
The result of polynomial evaluation is always a decimal number, regardless of the used radix used in the original representation.

## Slide 19: Examples

## Slide 20: Converting from ANY Radix to Decimal
Example: Converting from Radix 5 to Decimal
31245  = 3×53 + 1×52 + 2×51 + 4×50
= 3×125 + 1×25 + 2×5 + 4×1
= 375 + 25 + 10 + 4
= 41410
NOTE: Polynomial evaluation to convert from ANY radix to decimal.
The positional weights simply become powers of the radix.

## Slide 21: CONVERT BINARY TO DECIMAL (Using Polynomial Evaluation)
10112  = 1×23 + 0×22 + 1×21 + 1×20
= 1×8 + 1×2 + 1×1
= 8 + 2 + 1
= 1110

## Slide 22: EXTENDING POLYNOMIAL EVALUATION TO NUMBERS WITH A FRACTIONAL PART
10.0101112  = 1×21 + 0×20 + 0×2-1 + 1×2-2 + 0×2-3 + 1×2-4 + 1×2-5 + 1×2-6
= 1×21 + 1×2-2 + 1×2-4 + 1×2-5 + 1×2-6
= 2 + 1/4 + 1/16 + 1/32 + 1/64
= 2 + 0.25 + 0.0625 + 0.03125 + 0.015625
= 2.35937510

## Slide 23
36.728
= 3  81 + 6  80 + 7  8-1 + 2  8-2
= 24 + 6 + 0.875 + 0.03125
= 30.9062510
Example Converting Radix 8 to Decimal
Another fractional example

## Slide 24: AN EASIER METHOD
10.0101112
= (1×27 + 0×26 + 0×25 + 1×24 + 0×23 + 1×22 + 1×21 + 1×20)/26
= (128 + 16 + 4 + 2 + 1)/64
= 151/64
= 2.35937510
6 fractional digits
  Only a single division!
= 100101112 / 26
  Only a single division!

## Slide 25: Converting Fractions
Sometimes a fractional value has a finite representation in one number base, but not in another:
.333333333333
.0001100110011

## Slide 26: Representation Error
Computers store numbers using a fixed number of digits.
Some values does not have a finite representation in binary (e.g., )
Limiting the number of digits introduces a representation error:
.0001100 (8 bits) = .0976562510

## Slide 27: Group Work
Convert to decimal using polynomial evaluation:
76768
(unsigned) 1101 1111 1100 10112

## Slide 28: Group Work
Convert to decimal using polynomial evaluation:
76768 = 7×83 + 6×82 + 7×81 + 6×80
= 7×512 + 6×64 + 7×8 + 6×1
= 3,584 + 384 + 56 + 6
= 4,03010
(unsigned) 1101 1111 1100 10112

## Slide 29: Chapter 2 Binary Number Systems
Part 2: Unsigned Decimal to Binary Conversion

## Slide 30: Decimal to Binary Conversion
Example: 97.2510
Repeated multiplication
Repeated Division
1100001.012

## Slide 31: UNSIGNED DECIMAL TO BINARY CONVERSION
Separate problem into two parts:
Integer Part: Use repeated division
Fractional Part: Use repeated multiplication

## Slide 32: UNSIGNED DECIMAL TO BINARY Method 1: Integer Part (Repeated Division)
N N÷2 Remainder Result
13 6 1
6 3 0
3 1 1
1 0 1
1.
01.
101.
1101.
NOTE:
Repeated division may be used to convert from decimal to ANY radix.
Simply divide by the radix.
  Digits are produced right-to-left starting from the radix point.
STOP

## Slide 33: Decimal to Binary Conversion (Whole Part: Repeated Division)
Convert 9710 to base 2
97  2  | quotient = 48, | remainder = 1 (LSB)
48  2  | quotient = 24, | remainder = 0.
24  2  | quotient = 12, | remainder = 0.
12  2  | quotient = 6, | remainder = 0.
6  2  | quotient = 3, | remainder = 0.
3  2  | quotient = 1, | remainder = 1.
1  2  | quotient = 0 (Stop) | remainder = 1 (MSB)
Result =
1
1
0
0
0
0
12

## Slide 34: UNSIGNED DECIMAL TO BINARY Method 1: Fractional Part (Repeated Multiplication)
Product Whole Fractional
N (2×N) Part Part Result
.1 0.2 0 .2 .0
.2 0.4 0 .4 .00
.4 0.8 0 .8 .000
.8 1.6 1 .6 .0001
.6 1.2 1 .2 .00011
NOTE:
Repeated multiplication may be used to convert from decimal to ANY radix.
Simply multiply by the.
  Digits are produced left-to-right starting from the radix point.
Begins to repeat!

## Slide 35: Decimal to Binary Conversion (Fractional Part: Repeated Multiplication)
.1  2 
.2  2 
.4  2 
.8  2 
.6  2 
0.2 (fractional part = .2, whole part = 0)
0.4 (fractional part = .4, whole part = 0)
0.8 (fractional part = .8, whole part = 0)
1.6 (fractional part = .6, whole part = 1)
1.2 (fractional part = .2, whole part = 1)
Result = .000110011001100112…..
(How much should we keep?)

## Slide 36: Decimal to Binary Conversion (Fractional Part: Repeated Multiplication)
Example: 0.2510
.25  2 0.5 (fractional part = .5, whole part = 0)
.5  2 1.0 (fractional part = .0 (stop), whole part = 1)
Result = 0.0
Another example: 0.510
.5  2  1.0 (fractional part = .0 (stop), whole part = 1)
Result = .
0
12
12

## Slide 37: Group Work
Use repeated division & repeated multiplication:
145 . 62510
244 . 753410

## Slide 38: Group Work
Use repeated division & repeated multiplication:
145 . 62510 = 1001 0001 . 1010 00002
244 . 753410 = 1111 0100 . 1100 00002

## Slide 39: Chapter 2 Binary Number Systems
Part 4: Signed Number Conversions

## Slide 40: Two Interpretations
16710 1010 01112
-8910
Signed vs. unsigned is a matter of interpretation
Allowing both interpretations is useful: why?
Some data (e.g., count, age) can never be negative, and having a greater range is useful.
unsigned signed

## Slide 41: Changing the Signs
Sign+Magnitude:
+5 = 0101
Change 1 bit (only)
-5 = 1101
1010
+1
-5 = 1011
2’s Complement:
+5 = 0101
Invert
Increment

## Slide 42: Easier Hand Method (example 1)
+4 = 0100
-4 = 1100
Step 1:
Copy the bits from right to left and including the first 1.
Step 2:
Copy the inverse of the remaining bits.

## Slide 43: Easier Hand Method (example 2)
+5 = 0101
-5 = 1011
Step 1:
Copy the bits from right to left, through and including the first 1.
Step 2:
Copy the inverse of the remaining bits.

## Slide 44: Finding 2’s complement of fraction numbers
Example: if +5.75 = 0101.11002 find -5.75 in binary.
Solution:
Step 1: Remove the binary point 0101 1100
Step 2: Find the 2’s complement of 1010 0100
Step 3: Replace the binary point 1010.0100 = -5.75

## Slide 45: CONVERTING SIGNED DECIMAL TO TWO’S COMPLEMENT
Exercise: Find the 8-bit 2’s complement (minus) representation of:
2510

## Slide 46: CONVERTING SIGNED DECIMAL TO TWO’S COMPLEMENT
Convert the magnitude to unsigned binary:
      2510 = 16 + 8 + 1  1 10012
Zero extend to 8 bits:
      1 1001 0001 1001
Find the 2’s complement:
      0001 1001  1110 01112

## Slide 47
Example: 101100102 = ?10
Apply algorithm & add a negative sign
1. 101100102  -010011102
2. -(010011102) = -(64 + 8 + 4 + 2) = -7810
3. Answer: -7810
Converting 2’s complement numbers to decimal – Approach #1
101100102
010011102
inverse
inverse
inverse
inverse
inverse
inverse

## Slide 48: Changing the Sign of a Two’s Complement Number (Method 1)
if +1.2510 = 0001.01002
then -1.2510 = ????.????2
  Change every bit: 0001.0100
  1110.1011
  Then add 1 to the +1 least-significant 1110.1100 bit position.
. . .
  Simply changing the most-significant bit is NOT the same and doesn’t work!

## Slide 49: Changing the Sign of a Two’s Complement Number (Method 2)
100
If +1.2510 = 0001.01002
Then -1.2510 = ????.????2
Copy right-to-left 0001.0100
through first 1:
Copy opposite of all remaining bits:
1110.1
. . .
. . .

## Slide 50: Chapter 2 Binary Number Systems
Part 6: Power Relationships

## Slide 51: Hex

## Slide 52: MOTIVATION
Hexadecimal is a convenient short-hand for binary:
Hex (radix 16) numbers require 1/4th as many digits than their equivalent binary (radix 2) representation
Easier for humans  reduces transcription errors

## Slide 53: MOTIVATION
Conversion is trivial due to power relationship (16 = 24):
Each hex digit corresponds to a group of 4 binary digits.
Easy to convert: Groups are independent of each other.

## Slide 54: Hexadecimal Numbers (Radix = 16)
The number of digit symbols is determined by the radix (e.g., 16)
The value of the digit symbols range from 0 to 15 (0 to R-1).
The symbols are 0-9 followed by A-F.
Conversion between binary and hex is trivial!
Use as a shorthand for binary (significantly fewer digits are required for same magnitude).

## Slide 55: Hex/Binary Table

## Slide 56: Binary to Hex Conversions
000
Hex digits are in one-to-one groups of four:
11 1010 0101 0110 . 1110 0010 1111 1
3 A 5 6 . E 2 F 8
Start at binary point and identify groups of 4 bits
Zero-fill on left and right ends to complete the groups!
Conversion is a simple table lookup!
Works because 16 = 24 (power relationship)

## Slide 57: Example: Binary to Hex
Split into groups of 4, starting at radix point:
101 1010 . 1001 011
    Form groups working outward from the radix point!
Pad with 0’s to complete the groups:
0101 1010 . 1001 0110
3. Replace each group by equivalent hex digit:
5 A . 9 616
Hex | Binary
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
8 | 1000
9 | 1001
A | 1010
B | 1011
C | 1100
D | 1101
E | 1110
F | 1111

## Slide 58: Example: Hex to Binary
Convert F1.2C16 to Binary:
F 1 . 2 C
1111 0001 . 0010 11002
Hex | Binary
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
8 | 1000
9 | 1001
A | 1010
B | 1011
C | 1100
D | 1101
E | 1110
F | 1111

## Slide 59: Example: 110101.0101012 to Hex
Hex | Binary
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
8 | 1000
9 | 1001
A | 1010
B | 1011
C | 1100
D | 1101
E | 1110
F | 1111

## Slide 60: Example: 110101.0101012 to Hex
Use power relationship (16 = 24)
Form groups of 4 bits, starting at radix point:
11 0101 . 0101 01
0011 0101 . 0101 0100
Use Table to convert each group:
0011 0101 . 0101 0100
3 5 . 5 416
Hex | Binary | Hex | Binary
0 | 0000 | 8 | 1000
1 | 0001 | 9 | 1001
2 | 0010 | A | 1010
3 | 0011 | B | 1011
4 | 0100 | C | 1100
5 | 0101 | D | 1101
6 | 0110 | E | 1110
7 | 0111 | F | 1111

## Slide 61: Octal

## Slide 62: Octal/Binary Table
Octal | Binary
0 | 000
1 | 001
2 | 010
3 | 011
4 | 100
5 | 101
6 | 110
7 | 111
Octal and hexadecimal is a compromise between binary and decimal
Easier to read for humans
Was more important in the early days
Octal is not really used a lot
One the rights of a Unix/Linux file it is used

## Slide 63: Converting Octal (Base 8) to Hex
Hard way:
Convert octal to decimal (polynomial evaluation)
Convert decimal to hex (repeated division/multiplication)

## Slide 64: Converting Octal (Base 8) to Hex
Easy way:
Convert octal to binary using short-cut (8 = 23)
Convert binary to hex using short-cut (16 = 24)

## Slide 65: Converting Octal (Base 8) to Hex
Example: 12.658  ?16
12.658 = 001 010 . 110 1012 = 001010.1101012
001010.1101012 = 0000 1010 . 1101 01002 = 0A.D416

## Slide 66: Converting Octal (Base 8) to Hex
Convert octal to binary
Convert binary to hex

## Slide 67: Convert 21.348 to Binary
2 1 . 3 48
010 001 . 011 1002
Octal | Binary
0 | 000
1 | 001
2 | 010
3 | 011
4 | 100
5 | 101
6 | 110
7 | 111

## Slide 68: Convert AB.CD16 to base 8
1st: Base 16 to base 2 (16=24)
A B . C D16
1010 1011 . 1100 11012
2nd: Base 2 to base 8 (8=23)
10101011.110011012
010 101 011 110 011 010
010 101 011 110 011 010
2 5 3 6 3 28
.
.
Hex | Binary
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
8 | 1000
9 | 1001
A | 1010
B | 1011
C | 1100
D | 1101
E | 1110
F | 1111
Octal | Binary
0 | 000
1 | 001
2 | 010
3 | 011
4 | 100
5 | 101
6 | 110
7 | 111

## Slide 69: Convert FA.CE16 to base 8
1st: Base 16 to base 2 (16=24)
E16
F A . C
1111 1010 . 1100 11102
11111010.110011102
2nd: Base 2 to base 8 (8=23)
11111010.110011102
011 111 010 . 110 011 100
011 111 010 . 110 011 100
3 7 2 . 6 3 48
MOE
Hex | Binary
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
8 | 1000
9 | 1001
A | 1010
B | 1011
C | 1100
D | 1101
E | 1110
F | 1111
Octal | Binary
0 | 000
1 | 001
2 | 010
3 | 011
4 | 100
5 | 101
6 | 110
7 | 111

## Slide 70: Chapter 2 Binary Number Systems
Part 5: Worked Examples

## Slide 71: Convert unsigned 256 to decimal
Base R to Decimal  polynomial evaluation:
256 = 2x61 + 5x60
= 2x6 + 5x1
= 12 + 5
= 1710

## Slide 72: Convert unsigned 2510 to base 7
Whole #10 to Base R  repeated division (by 7):
25÷7  Q=3, R=4 3
2  Q=0, R=3
STOP
47
347
3÷7

## Slide 73: Convert unsigned .310 to base 7
Fractional #10 to Base R  repeated multiplication:
7 x .3 = 2.1 .2
7 x .1 = 0.7 .20
7 x .7 = 4.9 .204
7 x .9 = 6.3 .2046
Repeats! .20462046···

## Slide 74: Converting -25.7510 to 2’s Comp.
-25: 25 = 16 + 8 + 1
   011001
-25 = 100111
.75: .75 = .5 + .25
 .11
Combining results:
 100111.112
Checking (poly eval):
= -24.2510
Correct Method:
+25.75 = 16 + 8 + 1 + .5 + .25
= 011001.112
Find the negative representation:
 100110.01
Check:
100110.01 = 10011001/22
= (-128+16+8+1)/4
= -103/4
= -25.7510

## Slide 75: Convert -75.7510 to 2’s complement
1st: Get Binary Magnitude
7510 = 64 + 8 + 2 + 1
= 26 + 23 + 21 + 20
= 10010112
.7510 = .5 + .25
= 2-1 + 2-2
= .112
75.7510 = 1001011.112

## Slide 76: Convert -75.7510 to 2’s complement
2nd: Convert to 2’s Complement
+75.7510 = 01001011.112
Find ─75.7510:
2’s Comp: 10110100.01
The most-significant bit must be “1” (negative), so the minimum number of bits is 10.
Make sure the most-significant bit is 0.

## Slide 77: Convert 2’s Comp. 1001.01102 to decimal
Method #1
1001.0110 (< 0) - Find pos. equiv:
2’s Comp: 0110.1010
Get decimal = 4+2+.5+.125
= 6.62510
Add minus sign -6.62510

## Slide 78: Convert 2’s Comp. 1001.01102 to decimal
Method #2
Use poly. eval. w/neg. 1st term:
1001.0110:
= -8 + 1 + .25 + .125
= -7 + .375
= -6.62510

## Slide 79: Review Problems
Signed:
Convert -75.7510 to signed 2’s complement
Convert 1001.01102 from 2’s comp. to decimal
MOE

## Slide 80: Convert -75.7510 to 2’s complement
1st: Get Binary Magnitude
7510 = 64 + 8 + 2 + 1
= 26 + 23 + 21 + 20
= 10010112
7510 = .5 + .25
= 2-1 + 2-2
= .112
75.7510 = 1001011.112
2nd: Convert to 2’s Complement
+75.7510 = 01001011.112
10
Find ─75.75 :
Ignore “.”: | 0100101111
2’s Comp: | 1011010001
Restore “.”: | 10110100.01
The minimum number of
bits to represent -75.75 in binary is 10.
MOE

## Slide 81: Convert 2’s Comp. 1001.01102 to decimal
Method #1
1001.0110 (< 0) - Find pos. equiv:
Ignore “.” 2’s Comp: Restore “.”
10010110
01101010
0110.1010
Get decimal
= 4+2+.5+.125
= 6.62510
Add minus sign
-6.62510
Method #2
Use poly. eval. w/neg. 1st term:
1001.0110:
= -8 + 1 + .25 + .125
= -7 + .375
= -6.62510
MOE

## Slide 82: Practice Problems: NR1NR2
MOE
11010112 → ?16 110 1011 → 0110 1011 →6B16
11.010112 → ?16 11 . 0101 1 → 0011 . 0101 1000 → 3.5816
11010112 → ?8 1 101 011 → 001 101 011 →1538
11010.112 → ?8 11 010 . 11 → 011 010 . 110 →32.68
FACE16 → ?2 F A C E → 1111 1010 1100 11102 → 11111010110011102
Hex | Binary
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
8 | 1000
9 | 1001
A | 1010
B | 1011
C | 1100
D | 1101
E | 1110
F | 1111
Octal | Binary
0 | 000
1 | 001
2 | 010
3 | 011
4 | 100
5 | 101
6 | 110
7 | 111

## Slide 83: Chapter 2 Binary Number Systems
Part 3: Number Representations that use a Fixed Number of Digits

## Slide 84: Question:
Do you trust the used car salesman that tells you that the 1966 Mustang has only 13,000 miles that its odometer shows?
If not, what has happened?

## Slide 85: Rollover
Consequence of fixed precision.
– Computers use fixed precision!
Digits are lost on the left-hand end.
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1
Remaining digits are still correct.

## Slide 86: Rollover in Unsigned Binary
Consider an 8-bit byte used to represent an unsigned integer:
– Range: 0000 0000  1111 1111 (0  25510)
  Incrementing a value of 255 should yield 256, but this exceeds the range.
  Exceeding the range is known as rollover.

## Slide 87: Rollover in Signed Binary
In signed two’s complement with 8 bits adding 1 to -1 should result in 0 and it does
1111 1111 +
0000 0001
Carry = 1 0000 0000
It is a rollover with an accidental correct result.

## Slide 88
Rollover describes a pattern sequence behavior.
Overflow describes an arithmetic behavior.
– Resulted from an arithmetic operation
Whether or not rollover causes overflow depends on how the patterns are interpreted as numeric values!
Rollover is not a synonym for overflow!

## Slide 89: Rollover Causing Overflow

## Slide 90: Rollovers Versus Overflows
Summary:
Rollovers, that do not result in an overflow are ok.
  signed 1111 1111 + 1 = 0 (-1 + 1 = 0)
Overflows occur when you do some operation, and the result can not be represented with that many bits because the value is too large.
  unsigned 1111 1111 + 1 = 0 (256 + 1 = 0)
    Overflows must be handled

## Slide 91: Example of Unsigned Overflow Using 4-bit
1100 (12)
+ 0111 ( 7)
1 0011
Lost
(Result limited by word size)
0011 ( 3) wrong!
Range for 4 bits is 0 to 15
16 + 3 = 19

## Slide 92: Example of Signed Overflow Using 8-bit
Overflow is impossible when:
  adding numbers that have different signs.
  subtracting numbers that have same signs.
Overflow occurs when the magnitude of the result extends into the sign bit position:
0111 1111 (127) +
0000 0001 (1)
(0) 1000 0000 (-128)

## Slide 93: Another Example of Signed Overflow Using 8-bit
-12010 + 
-1710
sum: -13710
1000 10002 +
1110 11112
(1) 0111 01112
0111 01112 (keep 8 bits)
(+11910) wrong result!

## Slide 94: Summary
Situation | Example | Result | Flag
Unsigned rollover | 255 + 1 | 0 | Carry = 1
Signed overflow | +127 + 1 | −128 | Overflow = 1
Unsigned underflow/rollover | 0 − 1 | 255 | Carry/borrow indication
Signed underflow | −128 − 1 | +127 | Overflow = 1
Rollover is what the bits do. Overflow is what the signed interpretation tells you happened.
The same binary operation:
01111111 + 00000001 = 10000000
Can be interpreted as:
Unsigned: 127 + 1 = 128 → perfectly valid, no unsigned overflow
Signed: 127 + 1 = 128 → would be -1 (in 8-bit signed → overflow)

## Slide 95: Done

## Slide 96: … to here …