## Slide 1: CSEN20
Fall 2026
Introduction to Embedded Systems
Michael Schimpf, PhD, mschimpf@scu.edu

## Slide 2: Writing Functions
General Rules for Writing Assembler Functions:
  You can use any CPU registers from R0 to R12
  But If you use register R4-R11 you need to preserve them Example your function uses registers R4 and R5 then you need to PUSH {R4,R5} … POP {R4,R5}
  Call a function: BL funcName
  Passing parameters in: R0,R1,R2,R3
  Return from a function: BX LR
  If you call a function inside your function:
    Preserve LR on the stack: PUSH {LR} … POP {LR}
    Assume registers R0-R3 will be overwritten, no matter what
      For example, If you have something important in R3 and you need it later, and you call another function; you need to move it to a save register i.e. R4
    Return values are in R0 (32 bit) R0 and R1 (64 bit)

## Slide 3: ADDRESSING MODES (Calculating a Memory Address)
Immediate Offset Mode:
  [R0] // Adrs: R0
  [R0,4] // Adrs: R0+4
Register Offset Mode:
  [R0,R1] // Adrs: R0+R1
  [R0,R1,LSL 2] // Adrs: R0+4xR1
Pre-Indexed Mode (++var):
  [R0,4]!
Post-Indexed Mode (var++):
  [R0],4
Use these in ”loops” to reduce the number of instructions.
1. R0 = R0 + 4
2. Adrs: R0
1. Adrs: R0
2. R0 = R0 + 4

## Slide 4: Review: Pointer Arithmetic
int16_t *p16;
p16 = &a16[0];
p16 = p16 + 1;
int16_t a16[5];
a16[4] |  | a16[3] |  | a16[2] |  | a16[1] |  | a16[0] | 
1009 | 1008 | 1007 | 1006 | 1005 | 1004 | 1003 | 1002 | 1001 | 1000
p16 |  |  | 
2003 | 2002 | 2001 | 2000
p16 |  |  | 
1000 |  |  | 
2003 | 2002 | 2001 | 2000
p16 |  |  | 
1002 |  |  | 
2003 | 2002 | 2001 | 2000
Note: Each element of the array is an object of 2 bytes.
A pointer holds an address.
Address always 32-bits.
int16_t indicates the size and signees of the objects.
Plus 1 to a pointer, points to the next object.
Since each object is 2 bytes, the address must increase by 2.
32 bits

## Slide 5: Pointer Dereferencing
LDR R0,=p // R0 = &p (R0 = 2000)
LDR R1,[R0] // R1 = p (R1 = 1000)
LDR R2,[R1] // R2 = *p (R2 = 720)
LDR R3,[R1,4] // R3 = *(p + 1) (R3 = -3185)
LDR R4,[R1,8] // R4 = *(p + 2) (R4 = 1340)
1008 | 1340
1004 | -3185
1000 | 720
int32_t *p; // pointer to a 32-bit integer
2000 | 1000 | 
2000 | 1000 | 
addr
values
addr
addr to array

## Slide 6: Subscripted Array Reference
int32_t a[4]; // ‘a’ is an array of four 32-bit integers. // Each 32-bit integer is four bytes.
2488 | a[3]
2484 | a[2]
2480 | a[1]
2476 | a[0]
Address of a[k] must be computed at run-time:
LDR R0,=a // R0 = &a[0] LDR R1,=k // R1 = &k
LDR R1,[R1] // R1 = k
LDR R2,[R0,R1,LSL 2] // R2 = a[k]
32 bits
LDR R1,=a+8 // R1 = &a[2]
LDR R2,[R1] // R2 = a[2]
4 bytes
But it’s simpler when the subscript is a constant:
The symbol ‘a’ = &a[0], thus ‘a+8’ = &a[2]
address = Suppose k = 2: address = 2476 + 4x2 = 2484

## Slide 7: POINTERS & ARRAYS
Function in C | Function in assembly
// Init two arrays void f1(int8_t *p8, int16_t *p16, int32_t k32){ *(p8 + k32) = 0; *(p16 + k32) = 0; } | // Init two arrays f1: LDR R3,=0 STRB R3,[R0,R2] STRH R3,[R1,R2,LSL 1] BX LR
Function in C | Function in assembly
void f2(int8_t a8[], int16_t a16[], int32_t k32){ a8[k32] = 0; a16[k32] = 0; } | f2: LDR R3,=0 STRB R3,[R0,R2] STRH R3,[R1,R2,LSL 1] BX LR
Identical code!
Parameters are pointers
Parameters are arrays

## Slide 8
// Return the value *ps16 is pointing to
int16_t foo(int16_t *ps16){
return *ps16;
}
// R0 = ps16 (a 32-bit ptr to int16_t)
foo: LDRSH R0,[R0] // R0 = *ps16
BX LR
Note:
ps16 is a pointer to [an int16_t]
*ps16 is an int16_t
CPUlator week3: 06_one

## Slide 9
// next address to next element
int16_t *foo(int16_t *ps16){
return ps16 + 1; // pointer arithmetic!
}
// R0 = ps16 (a 32-bit ptr to int16_t)
foo: ADD R0,R0,#2 // R0 = ps16 + 1
BX LR
Note:
ps16 is a pointer to [an int16_t]
ps16+1 is a pointer to [the next int16_t]

## Slide 10
// Get the value ps16 is pointing to and add 1
int16_t foo(int16_t *ps16){
return *ps16 + 1 ; // parsed as (*ps16) + 1
}
// R0 = ps16 (a 32-bit ptr to int16_t)
foo: LDRSH R0,[R0] // R0 = *ps16
ADD R0,R0,#1 // R0 = *ps16 + 1
BX LR
Note:
ps16 is a pointer to [an int16_t]
*ps16 is an int16_t
*ps16+1 is regular integer arithmetic

## Slide 11
int16_t foo(int16_t *ps16){
return *(ps16 + 1); // pointer arithmetic
}
// R0 = ps16 (a 32-bit ptr to int16_t)
foo: ADD R0,R0,#2 // R0 = ps16 + 1
LDRSH R0,[R0] // R0 = *(ps16 + 1)
BX LR
foo: LDRSH R0,[R0,#2]
BX LR
Note:
ps16 is a pointer to [an int16_t]
ps16+1 is a pointer to [the next int16_t]
*(ps16+1) is the next int16_t
OR

## Slide 12
int32_t foo(int32_t a32[]){
return a32[1];
}
// R0 = a32 (a 32-bit ptr to int32_t)
foo: ADD R0,R0,#4 // R0 = a32 + 1
LDR R0,[R0] // R0 = a32[1]
BX LR
foo: LDR R0,[R0,#4]
BX LR
Note:
a32 is (same as) a pointer to [an int32_t]
a32[1] is same as *(a32+1)
a32+1 is a a pointer to [next int32_t]
*(a32+1) is the next int32_t
OR

## Slide 13
int32_t foo(int32_t a32[], int32_t k32){
return a32[k32];
}
// R0 = a32 (a 32-bit ptr to int32_t)
// R1 = k32 (a 32-bit int)
foo: LSL R1,R1,#2 // R1 = 4*k32
ADD R0,R0,R1 // R0 = a32 + 4*k32
LDR R0,[R0] // R0 = a32[k32]
BX LR
foo: LDR R0,[R0,R1,LSL #2]
BX LR
Note:
a32 is (same as) a pointer to [an int32_t]
a32[k32] is same as *(a32+k32)
a32+k32 is a pointer to [the k32th int32_t]
*(a32+k32) is the k32th int32_t
OR
CPUlator week3: 08_loopByteArray.s 09_loopWordArray.s

## Slide 14: Assignment 1

## Slide 15
https://cpulator.01xz.net/?sys=arm
// return R0 R0
uint16_t bar(uint16_t *pu16){
return *pu16;
}
Implement in Assembler: CPULator
CPUlator week3_Assignments: Assignment1.s

## Slide 16
bar: LDRH R0,[R0] BX LR
// return R0 R0
uint16_t bar(uint16_t *pu16){
return *pu16;
}
Implement in Assembler: CPULator
CPUlator week3_Assignments: Assignment1.s

## Slide 17: Assignment 2

## Slide 18
https://cpulator.01xz.net/?sys=arm
// next address to next element
// ret R0 R0
uint32_t *lopp(uint32_t *pu32){
return pu32 + 1; // pointer arithmetic!
}
Implement in Assembler: CPULator
CPUlator week3_Assignments: Assignment2.s

## Slide 19
// next address to next element
// ret R0 R0
uint32_t *lopp(uint32_t *pu32){
return pu32 + 1; // pointer arithmetic!
}
// R0 = pu32 (a 32-bit ptr to uint32_t)
lopp: ADD R0,R0,#4 // R0 = pu16 + 1
BX LR
Implement in Assembler: CPULator
CPUlator week3_Assignments: Assignment2.s

## Slide 20: Assignment 3

## Slide 21
// ret R0 R0 R1
uint8_t foo(uint8_t a8[], uint8_t k8){
return a8[k8];
}
Implement in Assembler: CPULator
CPUlator week3_Assignments: Assignment3.s

## Slide 22
// R0 R0 R1
uint8_t foo(uint8_t a8[], uint8_t k8){
return a8[k8];
}
// R0 = a8 (a 32-bit ptr to uint16_t)
// R1 = k8 (an 8-bit uint index)
foo: ADD R0,R0,R1 // R0 = a8 + k8
LDRB R0,[R0] // R0 = a8[k8]
BX LR
foo: LDRB R0,[R0,R1]
BX LR
OR
Implement in Assembler: CPULator
CPUlator week3_Assignments: Assignment3.s

## Slide 23: Assignment 4

## Slide 24
// Set two elements of an arrays index ku8 to 0xff
// R0 R1 R2
void form(uint32_t *pu32, uint16_t *pu16, uint8_t ku8){
*(pu32 + ku8) = 0xff;
*(pu8 + ku8) = 0xff;
}
Implement in Assembler: CPULator
CPUlator week3_Assignments: Assignment4.s

## Slide 25
// Init two arrays
// R0 R1 R2
void form(uint32_t *pu32, uint8_t *pu8, uint8_t ku8){
*(pu32 + ku8) = 0xff;
*(pu8 + ku8) = 0xff;
}
Implement in Assembler: CPULator
form: LDR R3,=0xff
STR R3,[R0,R2,LSL #2]
STRB R3,[R1,R2]
BX LR
CPUlator week3_Assignments: Assignment4.s

## Slide 26: Assignment 5

## Slide 27
// ret R0 R0 R1 int32_t funcIII(int32_t yi, int32_t er){ return funcIV(er + yi); }
Implement in Assembler: CPULator
CPUlator week3_Assignments: Assignment5.s

## Slide 28
// ret R0 R0 R1 int32_t funcIII(int32_t yi, int32_t er){ return funcIV(er + yi); }
Implement in Assembler: CPULator
funcIV:
PUSH {LR}
ADD R0,R1,R0
BL funcIV
POP {PC}
CPUlator week3_Assignments: Assignment5.s

## Slide 29: Assignment 6

## Slide 30
// ret R0 R0 int32_t funcV(int32_t kirk){ return kirk + funcVI(3, kirk); }
Implement in Assembler: CPULator
CPUlator week3_Assignments: Assignment6.s

## Slide 31
// ret R0 R0 int32_t funcV(int32_t kirk){ return kirk + funcVI(3, kirk); }
Implement in Assembler: CPULator
funcV:
PUSH {R4,LR}
MOV R4,R0
LDR R0,=3
MOV R1,R4
BL funcVI
ADD R0,R0,R4
POP {R4,PC}
CPUlator week3_Assignments: Assignment6.s

## Slide 32: Done