## Slide 1: CSEN20
Fall 2026
Introduction to Embedded Systems
Michael Schimpf, PhD, mschimpf@scu.edu

## Slide 2: Chapter 7 Manipulating Bits
Part 1: Specifying Bit Patterns

## Slide 3: Bit Patterns
A bit pattern (“mask”) is a string of 1’s and 0’s designed to select a subset of bits.
Bit patterns are used to:
  Test the value of one bit while ignoring others
  Set, clear, or invert the value of one bit without affecting others
  Extract or Insert a value stored in a subset of the bits of a word

## Slide 4: Useful Bit Patterns: (1 << k) = 2k (A single 1 shifted left k bits)
(12 << 4) = 000000012
000100002
= 1610
= 24
LDR R0,=(1<<4)
C++ Example 1

## Slide 5: Useful Bit Patterns: ~(1 << k) = ~2k (A single 0 shifted left k bits)
~(0b00000001 << 4) =
~(12 << 4) = 000000012
000100002
11011112
= ~00100002
= ~1610
= ~24
LDR R0,=~(1<<4)
C++ Example 1

## Slide 6: Useful Bit Patterns: (1 << k)-1 = 2k-1 (A string of k 1’s, preceded by all 0's)
26 = 010000002
-00000001
26-1 = 001111112
Six 1’s
LDR R0,=(1<<6)-1
C++ Example 1

## Slide 7: Chapter 7 Manipulating Bits
Part 2: Shift Instructions

## Slide 8: APPLICATIONS OF SHIFTING
Multiplication by 2k: 2k×A = A << k
Division by 2k: A÷2k = A >> k
Subscript Scaling: &a32[k] = &a32[0] + 4×k (LSL #2)
Creating Multiples: 7×A = 8×A - 1×A
7 = 8 - 1

## Slide 9: SHIFT INSTRUCTIONS
Instruction | Syntax | Operation | Flags | Notes
Logical Shift Left | LSL{S} Rd,Rn,bits | Rd = Rn << bits | N,Z,C | Zero fills
Logical Shift Right | LSR{S} Rd,Rn,bits | Rd = Rn >> bits | N,Z,C | Zero fills
Arithmetic Shift Right | ASR{S} Rd,Rn,bits | Rd = Rn >> bits | N,Z,C | Sign extends
Rotate Right | ROR{S} Rd,Rn,bits | Rd = Rn >> bits | N,Z,C | right rotate
Rotate Right w/Extend | RRX{S} Rd,Rn | Rd = Rn >> 1 | N,Z,C | right shift, fill with Carry
  Append "S" to capture the last bit shifted out in the carry (C) flag.
Only Rotate Right!

## Slide 10: Rotate Right
ROR
RRX
No Rotate Left!

## Slide 11: Instruction Sets
  An inline barrel shifter to preprocess one of the input registers (Operand2).
  It provides many types of shifts and rotates which can be applied to Operand2
    LSL R0,R0,#4 Logical left shift (<< in C)
    LSR R0,R0,#4 Logical shift right (>> in C)

## Slide 12: Instruction Sets
    ASR R0,R0,#4 - Arithmetic Shift Right (C signed division by a power of 2)
    ASR R0,R0,#4 - Arithmetic Shift Right
Positive Numbers
Negative Numbers

## Slide 13: Instruction Sets
    ROR R0,R0,#4 Rotate right (Bit rotate with wrap-around)
    RRX R0,R0,#1 Rotate Right Extended (33-bit rotate with wrap-around through carry bit)

## Slide 14: 3 PLACES WHERE SHIFT CAN BE USED
ROR R0,R1,R2 // R0 = R1 rotated right R2 times
ADD R0,R1,R2,LSR 3 // R0 = R1 + (R2 >> 3)
STR R0,[R1,R2,LSL 2] // R0 = mem32[R1+(R2*4)]
1. As a regular shift instruction.
2. To provide a pre-shifted copy of the value in a register as the last operand of an instruction.
3. To multiply a subscript (R2) by the # of bytes per element in a subscripted array reference.
The only context in which the shift count may be a variable (e.g., R2 here).
  Only a Logical Shift Left (LSL) by 1, 2 or 3 bits may be used in this context.

## Slide 15: Constants Dependent on Sign of R0
Instruction Sequence | Result left in R1: | 
 | When R0 < 0 | When R0 ≥ 0
LSR R1,R0,31 | +1 | 0
ASR R1,R0,31 | -1 | 0
MVN R1,R0,ASR 31 | 0 | -1
MVN R1,R0,LSR 31 | -2 | -1
LSR R1,R0,31 LSL R1,R1,k | +2k | 0
ASR R1,R0,31 LSL R1,R1,k | -2k | 0
ASR R1,R0,k-1 LSR R1,R1,32-k | +2k-1 | 0
CPULator: 10 LSRexamples.s
CPULator:
Experiment a bit
Check if correct
SIGNED VALUES!

## Slide 16: Chapter 7 Manipulating Bits
Part 3: 64-bit Shifts

## Slide 17: 64-BIT LOGICAL SHIFT LEFT (By 1 bit)
?
R1
R0
b63
b32
b31
b0
• • •
• • •
LSLS R0,R0,1
b63
b32
b00
b30
• • •
• • •
ADC R1,R1,R1
b62
b31
b00
b30
• • •
• • •
C
b31
b31
// uint64_t LSL64x1(uint64_t dword64) LSL64x1: LSLS R0,R0,1 // Shift LS 32 bits left by 1, capture C ADC R1,R1,R1 // Shift MS 32 bits left by 1, add C BX LR // Return
Only one example!

## Slide 18: Chapter 7 Manipulating Bits
Part 4: Bitwise Operations

## Slide 19: Review: Bitwise Operators
a = | a7 | a6 | a5 | a4 | a3 | a2 | a1 | a0
b = | b7 | b6 | b5 | b4 | b3 | b2 | b1 | b0
result = | c7 | c6 | c5 | c4 | c3 | c2 | c1 | c0
Each bit position of the result depends only on bits in the same position within the operands.

## Slide 20: Bitwise AND
Use bitwise AND to clear a single bit to 0
bits & ~(1 << 2)
a | b | a AND b
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
a = 0
a = 1
0
b
If a=0, output = 0
If a=1, output = b
b
a
 | b3 | b2 | b1 | b0
& | 1 | 0 | 1 | 1
 | b3 | 0 | b1 | b0
 | 1 | 1 | 1 | 1
& | 1 | 0 | 1 | 1
 | 1 | 0 | 1 | 1
Your number
Bit mask
Result
Example

## Slide 21: Bitwise AND
Use bitwise AND to isolate/test a single bit
bits & (1 << 2)
a | b | a AND b
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
a = 0
a = 1
0
b
If a=0, output = 0
If a=1, output = b
b
a
 | b3 | b2 | b1 | b0
& | 0 | 1 | 0 | 0
 | 0 | b2 | 0 | 0
 | 1 | 1 | 1 | 1
& | 0 | 1 | 0 | 0
 | 0 | 1 | 0 | 0
Your number
Bit mask
Result
Example

## Slide 22: Bitwise OR
Use bitwise OR to set a single bit to 1
bits | (1 << 2)
 | b3 | b2 | b1 | b0
¦ | 0 | 1 | 0 | 0
 | b3 | 1 | b1 | b0
a | b | a OR b
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
a = 0
a = 1
b
1
b
a
If a=0, output = b
If a=1, output = 1
 | 0 | 0 | 0 | 1
¦ | 0 | 1 | 0 | 0
 | 0 | 1 | 0 | 1
Your number
Bit mask
Result
Example

## Slide 23: Bitwise Exclusive-OR
Use bitwise XOR to change a single bit
bits ^ (1 << 2)
a | b | a XOR b
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
a = 0
a = 1
b
b
b
a
If a=0, output = b
If a=1, output = b
 | b3 | b2 | b1 | b0
^ | 0 | 1 | 0 | 0
 | b3 | b2 | b1 | b0
 | 1 | 0 | 0 | 1
^ | 0 | 1 | 0 | 0
 | 1 | 1 | 0 | 1
Your number
Bit mask
Result
Example
 | 1 | 1 | 0 | 1
^ | 0 | 1 | 0 | 0
 | 1 | 0 | 0 | 1
Your number
Bit mask
Result
Example
CPULator: XOE_EOR.s

## Slide 24: BITWISE INSTRUCTIONS
Instruction | Syntax | Operation | Flags
Bitwise AND | AND{S} Rd,Rn,Op2 | Rd = Rn & Op2 | N,Z,C
Bit Clear | BIC{S} Rd,Rn,Op2 | Rd = Rn & ~Op2 | N,Z,C
Bitwise OR | ORR{S} Rd,Rn,Op2 | Rd = Rn ¦ Op2 | N,Z,C
Exclusive OR | EOR{S} Rd,Rn,Op2 | Rd = Rn ^ Op2 | N,Z,C
Bitwise OR NOT | ORN{S} Rd,Rn,Op2 | Rd = Rn ¦ ~Op2 | N,Z,C
Move NOT | MVN{S} Rd,Rn | Rd = ~Rn | N,Z,C

## Slide 25: USING BITWISE INSTRUCTIONS
Set a bit to 1 without affecting other bits:
    X |= (1 << 5);
Clear a bit to 0 without affecting other bits:
    X &= ~(1 << 5);
Change a bit without affecting other bits.
    X ^= (1 << 5);
LDR R1,=x
LDR R0,[R1] ORR R0,R0,1<<5
    STR R0,[R1]
LDR R1,=x LDR R0,[R1] BIC R0,R0,1<<5
    STR R0,[R1]
LDR R1,=x
LDR R0,[R1] EOR R0,R0,1<<5
    STR R0,[R1]
C++ Example 2

## Slide 26: USING C BITWISE OPERATIONS
Test the value of a single bit in a word
    if ((word & (1 << 5)) != 0) …
Calculate remainder n%d when n≥0 and d= 2k
    rem = n % 16  rem = n & 0xF
Determine if an integer is an odd number
    (a % 2) == 1  (a & 1) != 0
  Calculating % takes more ARM CPU instructions than calculating &.
C++ Example 2

## Slide 27: Other Values Dependent on Sign of R0
Instruction Sequence | Result left in R2: | 
 | When R0 < 0 | When R0 ≥ 0
ADD R2,R1,R0,LSR 31 | R1 + 1 | R1
SUB R2,R1,R0,LSR 31 | R1 – 1 | R1
RSB R2,R1,R0,LSR 31 | 1 – R1 | R1
AND R2,R1,R0,ASR 31 | R1 | 0
BIC R2,R1,R0,ASR 31 | 0 | R1
ORR R2,R1,R0,ASR 31 | 1 | R1
ORN R2,R1,R0,ASR 31 | R1 | 1
EOR R2,R1,R0,ASR 31 | ~R1 | R1
Instruction Sequence | Result left in R2: | 
 | When R0 < 0 | When R0 ≥ 0
ADD R2,R1,R0,LSR 31 | R1 + 1 | R1
SUB R2,R1,R0,LSR 31 | R1 – 1 | R1
RSB R2,R1,R0,LSR 31 | 1 – R1 | 
AND R2,R1,R0,ASR 31 | R1 | 0
BIC R2,R1,R0,ASR 31 | 0 | R1
ORR R2,R1,R0,ASR 31 |  | R1
ORN R2,R1,R0,ASR 31 | R1 | 
EOR R2,R1,R0,ASR 31 | ~R1 | R1

## Slide 28: Chapter 7 Manipulating Bits
Part 5: Bitfields

## Slide 29: Trading Execution Time for Memory
Consider two unsigned integer values and , such that:
 12 bits  uint16_t (2 bytes)
0  20 bits  uint32_t (4 bytes)
But we can store both in a single 32-bit word and save 2 bytes:
uint32_t u32;
31 | 20 | 19 | 0
31 | 20 | 19 | 0

## Slide 30: Structure Bitfields
struct {
unsigned gender : 1; // 0 = male, 1 = female
unsigned siblings : 4; // 0-15
unsigned hair : 2; // 0=black, 1=brown, etc.
unsigned eyes : 2; // 0=brown, 1=blue, 2=green
unsigned weight : 9; // 0-511
unsigned ethnicity : 4; // 0=Caucasian,1=Asian, etc…
unsigned : 3; // unused
unsigned age : 7; // 0-127
} packed;
packed.eyes = color_code;
31 |  |  |  |  |  | 25 | 24 |  | 22 | 21 |  |  | 18 | 17 |  |  |  |  |  |  |  | 9 | 8 | 7 | 6 | 5 | 4 |  |  | 1 | 0
age |  |  |  |  |  |  | unused |  |  | ethnicity |  |  |  | weight |  |  |  |  |  |  |  |  | eyes |  | hair |  | siblings |  |  |  | 
LDR R2,=packed
LDR R0,[R2]
AND R0,R0,~(0b11 << 7)
LDR R1,=color_code
LDR R1,[R1]
AND R1,R1,0b11
ORR R0,R0,R1,LSL 7
STR R0,[R2]

## Slide 31: Extracting Unsigned Bitfield (Using LSL and LSR)
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 15 | 14 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
31 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 9 | 8 |  |  |  |  |  |  |  | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  |  |  |  |  |  | 
31 |  |  |  |  |  |  |  | 23 | 22 |  |  |  |  |  |  |  |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
LSL R1,R0,#8
LSR R1,R1,#23
32 – (lsb + width) = 8
32 – len = 23
width = 9
lsb = 15
unsigned zero-extension (all 0’s)
Extracted
bit-field
R0
R1
R1
C++ Example 3
CPULator: LSRexamples.s

## Slide 32: Extracting Signed Bitfield (Using LSL and ASR)
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 15 | 14 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | s |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
31 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 9 | 8 |  |  |  |  |  |  |  | 0
s | s | s | s | s | s | s | s | s | s | s | s | s | s | s | s | s | s | s | s | s | s | s | s |  |  |  |  |  |  |  | 
31 |  |  |  |  |  |  |  | 23 | 22 |  |  |  |  |  |  |  |  |  |  |  |  |  | 8 | 7 |  |  |  |  |  |  | 0
s |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
LSL R1,R0,#8
ASR R1,R1,#23
32 – (lsb + width) = 8
32 – len = 23
width = 9
lsb = 15
sign bit
2’s complement sign-extension
Extracted bit-field
R1
R1
R0

## Slide 33: Extracting Unsigned Bitfield (Using the UBFX instruction)
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 15 | 14 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
31 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 9 | 8 |  |  |  |  |  |  |  | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  |  |  |  |  |  | 
UBFX R1,R0,#15,#9
width = 9
lsb = 15
unsigned zero-extension (all 0’s)
Extracted
bit-field
R1
R0
CPULator: UBFX.s

## Slide 34: Extracting Signed Bitfield (Using the SBFX instruction)
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 15 | 14 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  | s |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
width = 9
lsb = 15
sign bit
31 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 9 | 8 |  |  |  |  |  |  |  | 0
s | s | s | s | s | s | s | s | s | s | s | s | s | s | s | s | s | s | s | s | s | s | s | s |  |  |  |  |  |  |  | 
SBFX R1,R0,#15,#9
2’s complement sign-extension
Extracted bit-field
R1
R0

## Slide 35
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 15 | 14 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
0 0 0 0 0 0 0 0 |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  |  | 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
31 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 9 | 8 |  |  |  |  |  |  |  | 0
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  | 
// Align a copy of source in R2; fill the rest with 0’s:
LSL R2,R0,#23
LSR R2,R2,#8
Inserting Bitfield from R0 into R1 (Using AND, LSL, LSR and ORR)
R1
R0
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 15 | 14 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
do not change |  |  |  |  |  |  |  | destination |  |  |  |  |  |  |  |  | do not change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
R2
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 15 | 14 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
unchanged |  |  |  |  |  |  |  | source |  |  |  |  |  |  |  |  | unchanged |  |  |  |  |  |  |  |  |  |  |  |  |  | 
R1
// Clear the destination field of R0 to all 0’s:
LDR R2,=0xFF007FFF
AND R1,R1,R2
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 15 | 14 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
unchanged |  |  |  |  |  |  |  | 0 0 0 0 0 0 0 0 0 |  |  |  |  |  |  |  |  | unchanged |  |  |  |  |  |  |  |  |  |  |  |  |  | 
R1
// Insert source from R2 into destinat- ion (R1):
ORR R1,R1,R2
23 bits
8 bits

## Slide 36
31 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  |  | 15 | 14 |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
Inserting Bitfield from R0 into R1 (Using the BFI instruction)
R0
R1
width = 9
lsb = 15
31 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 9 | 8 |  |  |  |  |  |  |  | 0
BFI R1,R0,#15,#9
width = 9
CPULator: BFI.s & BFI2.s

## Slide 37: BITFIELD INSTRUCTIONS & APPLICATIONS
Instruction | Syntax | Operation | Notes
Bit Field Clear | BFC Rd,lsb,width | Rd<bits>  0 | 
Bit Field Insert | BFI Rd,Rn,lsb,width | Rd<bits>  Rn<lsb’s> | 
Signed Bit Field Extract | SBFX Rd,Rn,lsb,width | Rd  Rn<bits> | Sign extends
Unsigned Bit Field Extract | UBFX Rd,Rn,lsb,width | Rd  Rn<bits> | Zero extends
CPULator: BFC.s

## Slide 38: Examples

## Slide 39: Examples (Implement in CPULator)

## Slide 40: Examples (Implement in CPULator)

## Slide 41: Examples (Implement in CPULator)

## Slide 42: Examples (Implement in CPULator)

## Slide 43: Examples (Implement in CPULator)

## Slide 44: Examples (Implement in CPULator)

## Slide 45: Examples (Implement in CPULator)
stop: B stop

## Slide 46: Examples (Implement in CPULator)

## Slide 47: Examples
https://cpulator.01xz.net/?sys=arm
(0xBB16)
(0x0033333316)
(0xBB33333316)

## Slide 48: Examples (Implement in CPULator)

## Slide 49: Chapter 7 Manipulating Bits
Part 6: Programming Tricks

## Slide 50: Register Swap Using Exclusive-OR (Uses 1 less register and no additional instructions)
// Standard method
// (requires 3rd register)
MOV R2,R0
MOV R0,R1
MOV R1,R2
// Exclusive-OR method
// No extra registers needed
EOR R0,R0,R1
EOR R1,R0,R1
EOR R0,R0,R1
0011
1011
R1
R0
1000
1011
0011
Exclusive-OR is 1 wherever the bits are different

## Slide 51: Selection Without a Branch
// Selection: R5 = (R0 < 0) ? R1 : R2
AND R3,R1,R0,ASR 31 // R3 = (R0 < 0) ? R1 : 0
BIC R4,R2,R0,ASR 31 // R4 = (R0 < 0) ? 0 : R2
ORR R5,R3,R4 // One of R3 or R4 will be all 0’s
a | b | a OR b
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
When a=0, output = b
When b=0, output = a
Consider Bitwise OR when at least one input is 0:

## Slide 52: A Fast Absolute Value Function
// uint32_t AbsValue(int32_t s32) AbsValue: // s32 < 0: else: EOR R1,R0,R0,ASR 31 // R1 = ~s32 R1 = s32 ADD R0,R1,R0,LSR 31 // R0 = ~s32 + 1 R0 = s32 + 0 BX LR // Return
  Fast! Avoids using making a compare and branch so that the instruction pipeline never stalls.
All 1’s if s32 < 0
All 0’s if s32 ≥ 0
1 if s32 < 0
0 if s32 ≥ 0
a | b | a XOR b
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
a = 0
a = 1
b
b
Recall that exclusive OR can be used to pass an operand through unmodified or inverted

## Slide 53: An Integer Power Function
// R0=x, R1=n,R2=result
  ipow: LDR R2,=1
loop: CBZ R1,done
LSRS R1,R1,1
IT CS
MULCS R2,R2,R0
MUL R0,R0,R0
B loop
done: MOV R0,R2
BX LR
uint32_t ipow(uint32_t x, uint32_t n){
uint32_t result;
result = 1;
while (n != 0){
if (n & 1) result *= x ;
n >>= 1 ;
x *= x ; // x1, x2, x4, x8, x16, etc.
}
return result;
}
()()() //

## Slide 54: Chapter 7 Manipulating Bits
Part 7: Bit-Banding

## Slide 55: APPLICATIONS OF BIT-BANDING
Fast access to individual bits in memory or I/O
Only 1 instruction required to access a single bit
No bitwise-AND, bitwise-OR, or shifting required

## Slide 56: APPLICATIONS OF BIT-BANDING
"Atomic" access to manage a "mutex".
Atomic: An atomic operation completes without preemption / interruption.
Mutex: Used in operating systems, networking and multi-threaded software to arbitrate access to a shared resource.

## Slide 57: BIT-BAND REGIONS & ALIASES
32MB Bit-Band Alias
22000000-23FFFFFF16
1MB Bit-Band Region
20000000-200FFFFF16
31MB of RAM
20100000-21FFFFFF16
64 MB of R/W Address Space
1 bit
1 word
1 bit
1 word
32MB Bit-Band Alias
42000000-43FFFFFF16
1MB Bit-Band Region
40000000-400FFFFF16
31MB of I/O
40100000-41FFFFFF16
64 MB of I/O Address Space
  Each individual bit in a bit-band region corresponds to an entire word in its bit-band alias.

## Slide 58: BIT-BAND MAPPING
 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
2000100016 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 0
…
A byte in the "bit-band region"
Corresponding 32-bit word(s) in the "bit-band alias region”
2202000C16 | 00000000 00000000 00000000 00000000
2202000816 | 00000000 00000000 00000000 00000000
2202000416 | 00000000 00000000 00000000 00000001
2202000016 | 00000000 00000000 00000000 00000000
2202001016 | 00000000 00000000 00000000 00000001
2202001416 | 00000000 00000000 00000000 00000001
2202001C16 | 00000000 00000000 00000000 00000001
2202001816 | 00000000 00000000 00000000 00000000

## Slide 59: FINDING THE ALIAS ADDRESS
Starting address of Bit-Band Region
  Example: Access bit 3 in 2000100016
  Bit-Band Region offset = 2000100016 – 2000000016 = 0100016
  Bit-Band Alias address = 2200000016 + 3210 × 0100016 + 4 × 3
  = 2200000016 + (0100016 << 5) + (3 << 2)
  = 2202000C16
31 |  |  |  |  |  | 25 | 24 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 5 | 4 |  | 2 | 1 | 0
0 | 0 | 1 | 0 | 0 | 0 | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 0
Bit-Band Alias address = 2200000016 + 32 × Bit-Band Region offset + 4 × bit number
  Read or write to this address accesses bit 3 at address 2000100016
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | 1 | 1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Recheck It is not correct!

## Slide 60: BIT-BAND FUNCTION
// uint32_t *BitBandAliasAddress(void *BitBandAdrs, int BitNum) ; // BitBandAdrs: The address of data in the bit band region // BitNum: The number (0-31) of the bit within the data .global BitBandAliasAddress .align .thumb_func BitBandAliasAddress: SUB R0,R0,0x20000000 // compute bit band offset LSL R0,R0,5 // insert offset into alias address ADD R0,R0,R1,LSL 2 // add 4 times the bit number (0-31) ADD R0,R0,0x22000000 // add base adrs of alias region BX LR .end

## Slide 61: Done