## Slide 1: CSEN20
Fall 2026
Introduction to Embedded Systems
Michael Schimpf, PhD, mschimpf@scu.edu

## Slide 2: Chapter 10
Floating-Point Emulation

## Slide 3: 32-bit IEEE Floating-Point Format
Exponent
Significand (fractional bits)
31
30
23
22
0
±
23 bits
8 bits
Precision: 23+1 bits ≈ 7 decimal digits
Range: ≈ 2±127 ≈ 10±38
Excess-127 format
20  01111111
Normalized (left-aligned): MS-Bit is always 1; never stored
Sign+Magnitude format:
0 if positive, 1 if negative
0
0111 1111
000 0000 0000 0000 0000 0000
Example: +1.0
=1

## Slide 4: Greater Range than 32-bit Integers
29 orders of magnitude difference!
Data Type | Max Magnitude | Representation
float |  | 7F7F FFFF
int32_t |  | 7FFF FFFF
uint32_t |  | FFFF FFFF
Data Type | Max Magnitude | Representation
float |  | 7F7F FFFF
int32_t |  | 7FFF FFFF
uint32_t |  | FFFF FFFF

## Slide 5: Greater Resolution than 32-bit Integers
Data Type | Min Non-Zero Value | Representation
float (subnormal) |  | 0000 0001
float (normal) |  | 0080 0000
int32_t |  | 0000 0001
uint32_t |  | 0000 0001
Data Type | Min Non-Zero Value | Representation
float (subnormal) |  | 0000 0001
float (normal) |  | 0080 0000
int32_t |  | 0000 0001
uint32_t |  | 0000 0001
45 orders of magnitude difference!

## Slide 6: Less Precision than 32-bit Integers
f32 = (float) u32 ;
0
1001 1110
000 0000 0000 0000 0000 0000
= 2,147,483,648.0
7 decimal digits (23+1 bits) of precision
1000 0000 0000 0000 0000 0000 0000 0000
u32 = (uint32_t) f32 ;
printf(“u32=%u\n”), u32) ; 2147483648
1000 0000 0000 0000 0000 0000 1111 1111
An exact representation requires 32 bits of precision
u32 = 2147483903 ;
discarded
24 bits
8 bits
uint32_t u32 ;
float f32 ;

## Slide 7: Interpreting 32-bit IEEE Float
Subnormal
Normal
Zero
Infinity
Not a Number
(underflow)
(overflow)
()
significand?
significand?
exponent?
Remove excess-127 bias:
11111110
Add hidden bit:

## Slide 8: Arithmetic Processing
special case?
& post-normalization

## Slide 9: Special Case Handling: Addition
Source: S. K. Raina, "FLIP: A Floating-Point Library for Integer Processors", Laboratoire de l'Informatique du Parallélisme, Sept. 12, 2006

## Slide 10: Special Case Handling: Multiplication
Source: S. K. Raina, "FLIP: A Floating-Point Library for Integer Processors", Laboratoire de l'Informatique du Parallélisme, Sept. 12, 2006

## Slide 11: Special Case Handling: Division
Source: S. K. Raina, "FLIP: A Floating-Point Library for Integer Processors", Laboratoire de l'Informatique du Parallélisme, Sept. 12, 2006

## Slide 12: Special Case Handling Determining Lookup Table Index
normal or subnormal
no
no
no
?

## Slide 13: Guard, Round & Sticky Bits
1.000 0000 0000 0000 0000 0000
0
0
0
e
0.000 0000 0000 0000 0000 0001
1
0
1
e
+
1.000 0000 0000 0000 0000 0001
1
0
1
e
1.000 0000 0000 0000 0000 0000
0
0
0
e
1.100 1000 0000 0000 0000 0000
0
0
0
e
+
G
R
S
(alignment)
(addition)
once set, stays set
used for rounding
24-bit significand
27-bit operand

## Slide 14: Round to Nearest Even
23-bit Significand | G | R | S | Rounding Action
X.XXX | 0 | X | X | ROUND DOWN (no change to significand bits)
X.XX0 | 1 | 0 | 0 | 
X.XX1 | 1 | 0 | 0 | ROUND UP (add 1 to LS-bit of the significand)
X.XXX | 1 | 0 | 1 | 
X.XXX | 1 | 1 | 0 | 
X.XXX | 1 | 1 | 1 | 
23-bit Significand | G | R | S | Rounding Action
 | 0 | X | X | ROUND DOWN (no change to significand bits)
 | 1 | 0 | 0 | 
 | 1 | 0 | 0 | ROUND UP (add 1 to LS-bit of the significand)
 | 1 | 0 | 1 | 
 | 1 | 1 | 0 | 
 | 1 | 1 | 1 | 

## Slide 15: Normalization
1.000 0000 0000 0000 0000 0000
e
1.000 0000 0000 0000 0000 0000
e
+
(addition)
10.000 0000 0000 0000 0000 0000
e
1.000 0000 0000 0000 0000 0000
e
(normalization)

## Slide 16: Done