## Slide 1: CSEN20
Fall 2026
Introduction to Embedded Systems
Michael Schimpf, PhD, mschimpf@scu.edu

## Slide 2: Chapter 5 Integer Arithmetic
Part 1: Addition and Subtraction

## Slide 3: ADDITION AND SUBTRACTION
Binary
0011
+1010
11012
  A single ADD (or SUB) instruction works for both unsigned and 2’s comp.
Unsigned
3
+10
1310
2’s Complement
(+3)
+(-6)
-310

## Slide 4: FLAGS Current Program Status Register (APSR)
26
0
29
28
30
31
27
N
Z
C
V
reserved
Overflow flag: A value of 1 indicates a 2’s complement overflow during an addition, subtraction or compare.
Carry flag: A value of 1 indicates a carry out during addition.
Zero flag: A value of 1 indicates a result (or difference) of zero
Negative flag: A value of 1 indicates a negative result
This subset is the Application Processor Status Register (APSR)
  Overflow during addition:
  Unsigned: C flag = 1
  2’s Comp: V flag = 1
  Overflow during subtraction:
  Unsigned: C flag = 0
  2’s Comp: V flag = 1

## Slide 5
Instruction | Format | Operation | Flags
Add | ADD{S} Rd,Rn,Op2 | Rd = Rn + Op2 | N,Z,C,V
Add with Carry | ADC{S} Rd,Rn,Op2 | Rd = Rn + Op2 + Carry | N,Z,C,V
Subtract | SUB{S} Rd,Rn,Op2 | Rd = Rn − Op2 | N,Z,C,V
Subtract with Carry | SBC{S} Rd,Rn,Op2 | Rd = Rn − Op2 − ~Carry | N,Z,C,V
Reverse Subtract | RSB{S} Rd,Rn,Op2 | Rd = Op2 − Rn | N,Z,C,V
ADD AND SUBTRACT INSTRUCTIONS
  "S" must be appended to affect the flags!
  "Op2" may only be a constant, a register, or a shifted register.

## Slide 6
// int64_t Add64(int64_t num1, int64_t num2) ; .global Add64 .align .thumb_func Add64: ADDS R0,R0,R2 // R0 = sum bits 31-0 ADCS R1,R1,R3 // R1 = sum bits 63-32 BX LR // Return .end
MULTIPLE-PRECISION ADDITION
  Use an ADC so that the carry is included in the second sum.
  Append "S" to ADD so it will record any carry out.
R1
R0
R2
R3
num1
num2
1st: ADDS
2nd: ADC
R1
R0
64bit Add

## Slide 7: EXAMPLE Implementing y = x + 5 ;
LDR R0,=x // R0 <-- &x (get the address of x)
LDR R0,[R0] // R0 <-- x (load the value of what R0 points)
ADD R0,R0,5 // R0 <-- R0 + 5 (add 5)
LDR R1,=y // R1 <-- &y (get the address of y)
STR R0,[R1] // R0 --> y (store R0 to address of y)
Common mistake:
LDR R0,=x+5 // R0
“x+5” is an address expression evaluated at time of assembly.
Try it with CPULator
https://cpulator.01xz.net/

## Slide 8: ARM Thumb-2

## Slide 9: ARM Thumb-2 Instruction Encodings
Two instruction sizes: 16-bits and 32-bits
Some operations are available in both versions
The assembler always uses a 16-bit version if available

## Slide 10: ADD Immediate
ADDS Rd,Rn,imm3
ADD{S} Rd,Rn,imm12
16-bit | 32-bit
Registers R0-R7 3-bit constants "S" required | Registers R0-R15 12-bit constants "S" optional
12bit

## Slide 11: ADD Register
ADDS Rd,Rn,Rm
ADD{S} Rd,Rn,Rm{,shift bits}
16-bit | 32-bit
Registers R0-R7 "S" required Rm not shifted | Registers R0-R15 "S" optional Shifted Rm optional

## Slide 12: Reducing Code Size = Faster Code
Use 16-bit instructions whenever possible.
Most 16-bit instructions require the letter “S”
  Always add “S” unless flags must not be changed
  Without “S”, instruction will be 32 bits wide!
Use the “narrow” 16-bit instruction if available (e.g., ADD.N)
  Doesn’t change the instruction, but
  Causes error message if there is no 16-bit version
Use the “wide” 32-bit instruction (e.g., ADD.W)

## Slide 13: Chapter 5 Integer Arithmetic
Part 2: Multiplication

## Slide 14: DECIMAL MULTIPLICATION
The product may require as many digits as the total # of digits!
99
×99
9,80110
9
×999
8,99110
999
×999
998,00110

## Slide 15: BINARY MULTIPLICATION
0011
×0010
0000 01102
1100
×1101 1001 11002
Product may require as many digits as the total # of digits.
A "double length product" uses the full product width:
2N bits  N bits × N bits
A "single length product" keeps only least-significant half: N bits  N bits × N bits
12
×13
15610 =
3
×2
610 =

## Slide 16: BINARY MULTIPLICATION
0000 11002
1001 11002
1100
×1101
12
×13
15610
-4
×-3
+1210
Unsigned
2’s comp
Binary
The signed and unsigned products are different!
Least-significant halves are the same!

## Slide 17: MULTIPLICATION IN C
The data type (and size) of the product is the same as operands. Thus: 32 bits × 32 bits  32 bits.
Consider how integer multiplication works in C:
  int32_t a, b;
  int32_t c;
  c = a * b;
  uint32_t x, y;
  uint32_t z;
  z = x * y;
The result is often stored in a variable of the same type, so a single-length product is sufficient.
Since the result is a single-length product, the same instruction can be used for signed and unsigned.
int32_t

## Slide 18: MULTIPLICATION IN C
Consider how integer multiplication works in C:
uint32_t a32, b32;
uint64_t c64;
c64 = a32 * b32;
c64 = a32 * c64;
Storing 32-bit product in a 64-bit variable simply extends the 32-bit result.
a32 is promoted to 64-bits to match c64; the 64x64 product requires a function
In C, operator results have the same data type as their operands.
C uses single-length products.
32-bit product
Zero-extended to 64 bits
Zero-extended to 64 bits to match data type of c64
64 bits x 64 bits

## Slide 19: MULTIPLICATION IN C
Consider how integer multiplication works in C:
  int8_t a8;
  int16_t b16;
  int32_t c32;
  c32 = a8 * b16;
On a 32-bit CPU, 8 and 16-bit operands are promoted to 32 bits
The product of a8 and b16 will becomes a 32x32 single-length product.
All integer multiplications produce either a single 32×32 instruction, or else a 64x64 library function call.
Each extended to 32 bits
32 bits x 32 bits

## Slide 20: MULTIPLICATION For Single-Length Products
MULS affects flags N and Z. No other multiply instruction affects the flags!
Instruction | Format |  | Operation
32-bit Multiply | MUL{S} | Rd,Rn,Rm | Rd = (int32_t) Rn×Rm
32-bit Multiply with Accumulate | MLA | Rd,Rn,Rm,Ra | Rd = Ra + (int32_t) Rn×Rm
32-bit Multiply & Subtract | MLS | Rd,Rn,Rm,Ra | Rd = Ra – (int32_t) Rn×Rm
All multiply instructions require their operands to be in registers.
Note: MLA and MLS use the product of the middle two registers.

## Slide 21: MULTIPLICATION OVERFLOW
Double-Length Products (signed or unsigned):
Overflow is not possible
Single-Length Unsigned Products:
Overflow occurs when the most-significant half of the double-length product is non-zero.
Single-Length Signed Products:
Overflow occurs when the most-significant half of the double-length product is NOT a sign-extension of the least-significant half.
1110 14
0111 ×7
0110 00102 9810
1110 (-2)
0111 ×(+7)
1111 00102 -1410
The overflow flag (V) is not affected! Recognizing overflow is virtually impossible if only a single-length product is available.
Overflow: The correct result exceeds the range.

## Slide 22: 64x64-bit MULTIPLICATION (Computing a 64-bit single-length product)
AHI (Upper Half)
32 bits
32 bits
ALO (Lower Half)
BHI (Upper Half)
BLO (Lower Half)
  A = 232AHI + ALO
  B = 232BHI + BLO
  A×B = (232AHI + ALO)(232BHI + BLO)
  = 264AHIBHI + 232(AHIBLO + ALOBHI) + ALOBLO
Not used
Not used
AHIBHI
× 264
  ALOBLO
LSW of AHIBLO
Not used
AHIBLO
× 232
Not used
ALOBHI
× 232
  3rd: UMULL(ALOBLO)
2nd: MLA(ALOBHI)
1st: MUL(AHIBLO)

## Slide 23: MULTIPLICATION Single-Length 64x64-Bit Product
// int64_t Mult64x64(int64_t a, int64_t b) ;
.global Mult64x64
.align
.thumb_func
Mult64x64: // R1.R0 = a, R3.R2 = b
MUL R1,R1,R2 // R1 = AHI x BLO
MLA R1,R0,R3,R1 // R1 += ALO x BHI
UMULL R0,R2,R0,R2 // R2.R0 = ALO x BLO
ADDS R1,R1,R2 // R1 += MSHalf of ALO x BLO
BX LR
.end
MSHalf = Most Significant Halfword

## Slide 24: MULTIPLICATION For Double-Length Products
Instruction | Format |  | Operation
64-bit Unsigned Multiply | UMULL | Rdhi,Rdlo,Rn,Rm | RdhiRdlo = (uint64_t) Rn×Rm
64-bit Unsigned Multiply with Accumulate | UMLAL | Rdhi,Rdlo,Rn,Rm | RdhiRdlo = RdhiRdlo + (uint64_t) Rn×Rm
64-bit Signed Multiply | SMULL | Rdhi,Rdlo,Rn,Rm | RdhiRdlo = (int64_t) Rn×Rm
64-bit Signed Multiply with Accumulate | SMLAL | Rdhi,Rdlo,Rn,Rm | RdhiRdlo = RdhiRdlo - (int64_t) Rn×Rm

## Slide 25: Multiplication Summary
32  32 x 32 (single length) | 64  32 x 32 (double length) | 64  64 x 64 (single length)
MUL R3,R1,R2 | UMULL R2,R3,R0,R1 | UMULL R4,R5,R0,R2 MLA R5,R1,R2,R5 MLA R5,R0,R3,R5
 | SMULL R2,R3,R0,R1 | 
R3=R1R2 | R3.R2=R0 R1 | R5.R4=R1.R0R3.R2
32  32 x 32 (single length) | 64  32 x 32 (double length) | 64  64 x 64 (single length)

## Slide 26: Chapter 5 Integer Arithmetic
Part 3: Division

## Slide 27: DIVISION IN C
Consider how integer division works in C:
  int8_t a8;
  int16_t b16;
  int32_t c32;
  int64_t d64;
  ... = a8 / b16;
  ... = d64 / c32;
8 and 16-bit operands are promoted to 32 bits; this becomes a single 32÷32 divide instruction that produces a 32-bit quotient.
c32 is promoted to 64 bits to match d64; this becomes a library function call for 64÷64 division that returns a 64-bit quotient.
All integer divisions produce either a single 32÷32 instruction, or else a library function call for 64÷64.

## Slide 28: SINGLE-LENGTH DIVISION
1111 00002
÷0000 01002
Two different instructions for signed vs unsigned division.
Instruction | Format | Operation
Unsigned Divide | UDIV Rd,Rn,Rm | Rd = (uint32_t) Rn ÷ Rm
Signed Divide | SDIV Rd,Rn,Rm | Rd = (int32_t) Rn ÷ Rm
24010
÷410
6010
Unsigned:
(-1610)
÷(+410)
-410
2’s complement:
0011 11002
1111 11002

## Slide 29: DIVISION OVERFLOW
The smaller range of a single-length dividend reduces the # of operand combinations that result in an overflow.
Two possibilities:
Unsigned or 2's complement: Division by zero
2's complement: Full-scale negative (-231) divided by -1,
There is no hardware detection of overflow during integer division! V flag (overflow) is not affected!
Overflow during division =>
the result exceeds the quotient’s range.

## Slide 30
remainder:
// R0 <-- dividend // example = 14
// R1 <-- divisor // example = 3
SDIV R2,R0,R1 // R2 = R0 / R1 // 4 = 14 / 3
MLS R3,R1,R2,R0 // R3 = R0 – (R1*R2) // 2 = 14 – (3*4)
BX LR
Operation | Quotient | Remainder
(+14) ÷ (+3) | +4 | +2
(+14) ÷ (-3) | -4 | +2
(-14) ÷ (+3) | -4 | -2
(-14) ÷ (-3) | +4 | -2
Computing A Remainder
remainder = dividend – divisor × quotient

## Slide 31: Chapter 5 Integer Arithmetic
Part 4: Summary of Integer Arithmetic Instructions

## Slide 32: Integer Addition
Instructions: ADD{S}, ADC{S}
Format Examples:
  ADD R0,R1,#5 // R0 = R1 + 5
  ADD R0,R1,R2 // R0 = R1 + R2
  ADD R0,R1,R2,LSL #2 // R0 = R1 + (R2 << 2)
Flags: Append “S” to capture result characteristics in NCVZ
Overflow:
  Unsigned: Carry Flag (C) = 1
  Signed: Overflow Flag (V) = 1 (Set when CN≠CN-1)
Multiple precision addition: ADDS  ADC

## Slide 33: Integer Subtraction
Instructions: SUB{S}, SBC{S}, RSB{S}
Format Examples:
  SUB R0,R1,#5 // R0 = R1 - 5
  SUB R0,R1,R2 // R0 = R1 - R2
  SUB R0,R1,R2,LSL #2 // R0 = R1 - (R2 << 2)
Flags: Append “S” to capture result characteristics in NCVZ
Overflow:
  Unsigned: Carry Flag (C) = 0
  Signed: Overflow Flag (V) = 1 (Set when CN≠CN-1)
Multiple precision subtraction: SUBS  SBC

## Slide 34: Single-Length 32x32 Integer Multiplication
Instructions: MUL{S}, MLA, MLS
Signed vs. Unsigned: Use same instruction
Format Examples:
  MUL R0,R1,R2 // R0 = R1 × R2
  MLA R0,R1,R2,R3 // R0 = R3 + R1 × R2
  MLS R0,R1,R2,R3 // R0 = R3 - R1 × R2
Flags: Append “S” (only MUL) to capture result characteristics in N and Z flags
Overflow: May happen but impossible to detect!

## Slide 35: Double-Length 32x32 Integer Multiplication
Instructions: UMULL, SMULL, UMLAL, SMLAL
Signed vs. Unsigned: Use different instructions!
Signed Instruction Formats:
  SMULL R0,R1,R2,R3 // R0.R1 = R2 × R3
  SMLAL R0,R1,R2,R3 // R0.R1 = R0.R1 + R2 × R3
Unsigned Instruction Formats:
  UMULL R0,R1,R2,R3 // R0.R1 = R2 × R3
  UMLAL R0,R1,R2,R3 // R0.R1 = R0.R1 + R2 × R3
Flags: Unaffected!
Overflow: Can’t happen

## Slide 36: Single-Length 32÷32 Integer Division
Instructions: SDIV, UDIV
Signed vs. Unsigned: Use different instructions!
Signed Instruction Format:
  SDIV R0,R1,R2 // R0 = R1 ÷ R2
Unsigned Instruction Format:
  UDIV R0,R1,R2 // R0 = R1 ÷ R2
Flags: Unaffected
Overflow:
  Division by zero
  Full-scale negative divided by -1

## Slide 37: Done

## Slide 38: … to here …