## Slide 1: CSEN20
Fall 2026
Introduction to Embedded Systems
Michael Schimpf, PhD, mschimpf@scu.edu

## Slide 2: Chapter 3 Writing Functions in Assembly
Part 1: Embedded Application Development

## Slide 3: Assembler in General
Most of a program is written in a high-level language such as C
  easier to implement
  easier to understand
  easier to maintain
Only a few functions are written in assembly
  to improve performance, or
  because it’s difficult or impossible to do in a high-level language.

## Slide 4: Creating a Program
Linker
Executable Program
Library code
Compiler
Assembler
Object code
Object code
Library header files
C sourcecode
ASM sourcecode
Most of code, including function main
A few small functions

## Slide 5: ARM Cortex M4 Core Registers
General-Purpose Register

## Slide 6: Consequence
Assembly functions must be compatible with:
How the C compiler invokes the execution of an assembly function (i.e. passes the execution control to the function)
How the C compiler passes parameters to assembly functions
How the C compiler expects to receive results from assembly functions
How the C compiler uses CPU registers
  Knowing and agreeing on what register is used for what purpose.
.c
.s

## Slide 7: Consequence
Assembly functions must be compatible with the C compiler to:
  Call a function (compiler/assembler BL funcName)
  Pass parameters (R0,R1,R2,R3)
  Use CPU registers (R0 to R12)
  Receive return value (R0,R1)

## Slide 8: Consequence
Assembly functions must be compatible with the C compiler to:
  If you use R4 to R11, you need to preserve them!
  Return with BX LR
  If your function calls a function BL Label. You need to: PUSH {LR} and POP {LR}

## Slide 9: Example Source Files
// Main Program written in
#include <stdio.h>
#include <stdint.h>
#include "library.h"
extern uint32_t Add1(uint32_t x);
int main(void){
uint32_t strt, stop, before, after;
InitializeHardware(HEADER, PROJECT_NAME);
before = 0;
while (1) { // Never exit
strt = GetClockCycleCount();
after = Add1(before);
stop = GetClockCycleCount();
printf("Before = %u\n", (unsigned) before);
printf(" After = %u\n", (unsigned) after);
printf("CPU Clock Cycles: %u\n", (unsigned) (stop - strt));
WaitForPushButton();
ClearDisplay();
before = after;
}
}
//Function written in Assembly
.syntax unified
.cpu cortex-m4
.text
.thumb_func
.align 2
// uint32_t Add1(uint32_t x);
.global Add1
Add1: ADD R0, R0,1 // Return x +1
BX LR
.end

## Slide 10: void InitializeHardware(char *, char *) ;
// Main Program written in
#include <stdio.h>
#include <stdint.h>
#include "library.h"
extern uint32_t Add1(uint32_t x);
int main(void){
uint32_t strt, stop, before, after;
InitializeHardware(HEADER, PROJECT_NAME);
before = 0;
while (1) { // Never exit
strt = GetClockCycleCount();
after = Add1(before);
stop = GetClockCycleCount();
printf("Before = %u\n", (unsigned) before);
printf(" After = %u\n", (unsigned) after);
printf("CPU Clock Cycles: %u\n", (unsigned) (stop - strt));
WaitForPushButton();
ClearDisplay();
before = after;
}
}
Must be executed first
Initializes:
  Processor
  CPU clock cycle counter
  the display
  user push button.
Creates stack and heap
Initializes static variables.
Formats display area

## Slide 11: uint32_t GetClockCycleCount(void) ;
// Main Program written in
#include <stdio.h>
#include <stdint.h>
#include "library.h"
extern uint32_t Add1(uint32_t x);
int main(void){
uint32_t strt, stop, before, after;
InitializeHardware(HEADER, PROJECT_NAME);
before = 0;
while (1) { // Never exit
strt = GetClockCycleCount();
after = Add1(before);
stop = GetClockCycleCount();
printf("Before = %u\n", (unsigned) before);
printf(" After = %u\n", (unsigned) after);
printf("CPU Clock Cycles: %u\n", (unsigned) (stop - strt));
WaitForPushButton();
ClearDisplay();
before = after;
}
}
Returns the number of processor clock cycles since initialization.
start = GetClockCycleCount();
// do some calculation here
stop = GetClockCycleCount();
printf("Cycles=%d\n", stop-start);
Cycles=1788
STM32F429I-DISCO
GetClockCycles

## Slide 12: void WaitForPushButton(void) ;
// Main Program written in
#include <stdio.h>
#include <stdint.h>
#include "library.h"
extern uint32_t Add1(uint32_t x);
int main(void){
uint32_t strt, stop, before, after;
InitializeHardware(HEADER, PROJECT_NAME);
before = 0;
while (1) { // Never exit
strt = GetClockCycleCount();
after = Add1(before);
stop = GetClockCycleCount();
printf("Before = %u\n", (unsigned) before);
printf(" After = %u\n", (unsigned) after);
printf("CPU Clock Cycles: %u\n", (unsigned) (stop - strt));
WaitForPushButton();
ClearDisplay();
before = after;
}
}
Causes program to pause and wait for user to push the blue push button on the board.

## Slide 13: void ClearDisplay(void) ;
// Main Program written in
#include <stdio.h>
#include <stdint.h>
#include "library.h"
extern uint32_t Add1(uint32_t x);
int main(void){
uint32_t strt, stop, before, after;
InitializeHardware(HEADER, PROJECT_NAME);
before = 0;
while (1) { // Never exit
strt = GetClockCycleCount();
after = Add1(before);
stop = GetClockCycleCount();
printf("Before = %u\n", (unsigned) before);
printf(" After = %u\n", (unsigned) after);
printf("CPU Clock Cycles: %u\n", (unsigned) (stop - strt));
WaitForPushButton();
ClearDisplay();
before = after;
}
}
Sine Function
STM32F429I-DISCO
Erases the scrollable area of the display.

## Slide 14: Chapter 3 Writing Functions in Assembly
Part 2: Function Call and Return

## Slide 15: Instruction Fetch
Instructions
(as well as any Data, the Stack, and the Heap)
Address
Data
Instruction Register
Memory
CPU
Program Counter (PC)
+1

## Slide 16: Memory Layout (Recall)
Stack: automatic storage (LIFO)
Dynamic data: heap
– i.e.: malloc in C, new in Java/C++
Static data: global variables
– e.g., static variables in C, constant arrays and strings
Text: program code

## Slide 17: FUNCTION CALL AND RETURN Simple Call-Return in C
● ● ● f1(); ● ● ● | void f1(void){ ● ● ● return; }
Suspend the current sequence
Record the return address
Transfer control to the function
Execute the function
Use the recorded return address to jump back.
Branch with Link Instruction (BL)
Branch Indirect Instruction (BX)

## Slide 18: FUNCTION CALL AND RETURN ARM instructions used to call and return from functions
Instruction | Format |  | Operation
Branch with Link | BL | label | Function Call: LR  return address, PC  address of label
Branch Indirect | BX | LR | Function Return: PC  LR
LR (aka R14) and PC (aka R15) are two of the 16 registers inside the CPU.
LR is the “Link Register” – used w/function calls to hold the return address
PC is the “Program Counter” – holds the address of the next instruction.

## Slide 19: FUNCTION CALL AND RETURN Simple Call-Return in Assembly
● ● ● BL f1 ● ● ● | f1: ● ● ● BX LR
BL (Branch with Link) instruction saves the address in the Link Register (LR).
The “Branch Indirect” instruction (BX) copies the address from LR into PC.
Only one Link Register!

## Slide 20: FUNCTION CALL AND RETURN Nested Call-Return in Assembly
● ● ● BL f1 ● ● ● | f1: ● ● ● BL f2 ● ● ● BX LR | f2: ● ● ● BX LR
Modifies the link register (LR), writing over f1’s return address!
Saves LR on the stack.
Restores LR from the stack.
PUSH {LR}
POP {LR}
Saves the return address in LR
Copies the return address from LR to PC

## Slide 21: FUNCTION CALL AND RETURN ARM instructions used in functions that call other functions
Instruction | Format |  | Operation
Push registers onto stack | PUSH | register list | SP = SP – 4 × #registers Copy registers to mem[SP]
Pop registers from stack | POP | register list | Copy mem[SP] to registers, SP = SP + 4 × #registers
SP is one of the 16 CPU registers (R13)
holds the address of the top of the stack.
1000 | Pushed data
996 | Pushed data
992 | Top of stack
988 | 
984 | 
980 | 
976 | 
972 | 
SP | 992
(register R13)
(memory)
Unused Stack
Space
“register list” format: { reg, reg, reg-reg, …}
IMPORTANT! Registers in the list must be listed in numerical order.

## Slide 22: Optimizing Function Calls
f1: PUSH {LR} // StackLR
●
●
●
BL f2
●
●
●
POP {PC} // PCStack
f1: PUSH {LR} // StackLR
●
●
●
BL f2
●
●
●
POP {LR} // LRStack
BX LR // PC=LR

## Slide 23: Optimizing Function Calls
● ● ● BL f1 ● ● ● | f1: ● ● ● B f2 | f2: ● ● ● BX LR
● ● ● BL f1 ● ● ● | f1: ● ● ● BL f2 BX LR | f2: ● ● ● BX LR
PUSH {LR}
POP {LR}

## Slide 24: Stack Alignment
MyFunc: PUSH {LR}
...
BL printf
...
POP {PC}
Some library functions and functions compiled from a high-level language require that SP mod 8 = 0 when they are called – i.e., that the stack be double word (8-byte) aligned.
Problem: The compiler ensures that the stack pointer is always a multiple of 8 when it calls a function.
This will not true if your function calls another function after pushing an odd number of registers.

## Slide 25: Stack Alignment
MyFunc: PUSH {R3,LR}
...
BL printf
...
POP {R3,PC}
Some library functions and functions compiled from a high-level language require that SP mod 8 = 0 when they are called – i.e., that the stack be double word (8-byte) aligned.
Solution: When writing a function that calls a library function or a function that was compiled from a high-level language, always push and pop an even number of registers.
Register R3 is used since there is no other reason to push it.

## Slide 26: Chapter 3 Writing Functions in Assembly
Part 3: Passing Parameters and Saving the Return Value

## Slide 27: ARM PROCEDURE CALL STANDARD Registers used as input parameters
Register | AAPCS Name | Usage
R0 | A1 | 1st parameter
R1 | A2 | 2nd parameter
R2 | A3 | 3rd parameter
R3 | A4 | 4th parameter
One register is used for each 8, 16 or 32-bit parameter.
A sequential register pair is used for each 64-bit parameter.
APCS ARM Procedure Call Standard,
AAPCS of Procedure Call Standard for the ARM Architecture

## Slide 28: PARAMETER PASSING void foo(int8_t, int32_t, int64_t) ;
C Function Call | Compiler Output
LDR R0,=x8 // R0 <-- &x8
LDRSB R0,[R0] // R0 <-- x8
LDR R1,=y32 // R1 <-- &y32
LDR R1,[R1] // R1 <-- y32
LDR R2,=z64 // R2 <-- &z64
LDRD R2,R3,[R2] // R3.R2 <-- z64
BL foo
●
●
●
LDR R0,=5 // R0 <-- 5
LDR R1,=-10 // R1 <-- -10
LDR R2,=20 // R3.R2 <-- 20
LDR R3,=0
BL foo
int8_t x8;
int32_t y32;
int64_t z64;
●
●
foo(x8, y32, z64);
●
●
foo(5, -10, 20);
●
●
  Inside foo, you must use the register copies of the actual arguments.

## Slide 29: HOW COMPILER HANDLES RETURN VALUES Promoting a return value from 8 to 16, 32 or 64 bits
If you do variables in Assembler
In C: int a=0xaa;
int b=0xbbbb;
int c=0xcccccccc;
Long int d=0xEEEEE...DDDD…;

## Slide 30: Why 2 Instructions to load a variable?
Instructions are at most 32 bits wide.
  Some bits are used to specify the operation code
  Some bits are used to specify register operands
All addresses are 32 bits wide.
Instructions itself have no room for a 32-bit address
31 |  |  | 0
31 | 0
Address of x | 
LDR reg,x
LDR Opcode
Register #
NOT ENOUGH BITS LEFT OVER!
32 bits wide

## Slide 31: Why 2 Instructions to load a variable?
Solution: Use an address “displacement”
  Displacement: Address distance from instruction to operand
  Assumes operand is at an address near the instruction
  Displacements = smaller numbers  fewer bits
Address 1000000 |  | LDR | R0,x
 |  | ● | 
 |  | ● | 
 |  | ● | 
Address 1000500 | x: | .word | 1000
Displacement = 500

## Slide 32: Why 2 Instructions to load a variable?
Instructions are stored in read-only memory
Variables are stored in read/write memory
Instructions and variables are too far apart for a small displacement.
The magnitude of the displacement would require too many bits, to fit inside an instruction.
Address Range:
20000000-2002FFFF
400,556,03210 bytes
Address Range:
0800000-081FFFFF
Read/Write Memory
Read-Only Memory
(Variables, Stack, and Heap)
(Instructions & Constants)
(requires 29 bits!)

## Slide 33: Why 2 Instructions to load a variable?
Solution:
  Copy the operand address (which is a read-only constant) into a register
  then …
  Use that register to provide the address in a second instruction
x: .word 1000
Unused Addresses
In assembly, the value represented by the identifier “x” comes from the symbol table, and is the address where the variable x is located.
“x” is a variable whose content is 1000
Read/Write Memory
Read-Only Memory
LDR R0,temp
LDR R1,[R0]
●
●
temp: .word x
LDR R0,=x
LDR R1,[R0]

## Slide 34: ARM PROCEDURE CALL STANDARD Registers used to return function result
Register | AAPCS Name | Usage
R0 | A1 | 8, 16 or 32-bit result, or the least-significant half of a 64-bit result
R1 | A2 | The most-significant half of a 64-bit result

## Slide 35: SAVING THE RETURN VALUE Functions that return an 8, 16 or 32-bit result
Functions must provide a full 32-bit representation of return value, even for 8 and 16-bit results.
UPDATE THIS SLIDE!! UPDATE THIS SLIDE!! UPDATE THIS SLIDE!!

## Slide 36: PREPARING THE RETURN VALUE Functions that return an 8 or 16-bit result
uint32_t Add1(uint32_t x){
return x + 1;
}
Add1(254) = 255
Add1(255) = 256
Add1(256) = 257
uint8_t Add1(uint8_t x){
return x + 1;
}
Add1(254) = 255
Add1(255) = 0 Why?
Add1(256) = 1 Why?
-1 = 255

## Slide 37: PREPARING THE RETURN VALUE Functions that return an 8 or 16-bit result
uint8_t Add1(uint8_t x){
return x + 1;
}
Add1: ADD R0,R0,1
UXTB R0,R0
BX LR
Remember: 0 ≤ uint8_t ≤
So, adding 1 to 255 in 8 bits yields 0 due to overflow:
(x is zero-extended to fill R0)
Add 1:
11111111 +00000001
00000000
Input parameter
Return value must be zero-extended from 8-bit result

## Slide 38: Chapter 3 Writing Functions in Assembly
Part 4: Preparing and Using the Return Value

## Slide 39: PREPARING THE RETURN VALUE Functions that return an 8 or 16-bit result
Instruction | Operation | operand2 options:
UXTB Rd, operand2 | Rd Zero extend operand2<7..0> | Rm (a register) Rm,ROR constant (constant=8, 16 or 24)
UXTH Rd, operand2 | Rd Zero extend operand2<15..0> | 
SXTB Rd, operand2 | Rd Sign extend operand2<7..0> | 
SXTH Rd, operand2 | Rd Sign extend operand2<15..0> | 
Instruction | Operation | operand2 options:
UXTB Rd, operand2 |  | Rm (a register) Rm,ROR constant (constant=8, 16 or 24)
UXTH Rd, operand2 |  | 
SXTB Rd, operand2 |  | 
SXTH Rd, operand2 |  | 

## Slide 40: Summary
Call functions using Branch with Link (BL)
  Saves the return address in Link Register (LR)
  Copies the target address into Program Counter (PC)
Return from a function using BX LR
  Copies the return address from LR back into PC

## Slide 41: Summary
Writing functions that call other functions:
  Using BL to call another function changes LR
  Use PUSH {LR} / POP {LR} to preserve LR
Pass parameters using registers R0-R3
  64-bit parameters in consecutive register pairs
Return 8, 16 and 32 bit results using R0
  64-bit result returned in R1.R0 register pair

## Slide 42: Chapter 3 Writing Functions in Assembly
Part 5: Coding Conventions

## Slide 43: REGISTER USAGE CONVENTIONS ARM PROCEDURE CALL STANDARD
Register | AAPCS Name | Usage | Notes
R0 | A1 | Argument / result /scratch register 1 | Do not have to preserve original contents
R1 | A2 | Argument / result /scratch register 2 | 
R2 | A3 | Argument / scratch register 3 | 
R3 | A4 | Argument / scratch register 4 | 
R4 | V1 | Variable register 1 | Must preserve original contents
R5 | V2 | Variable register 2 | 
R6 | V3 | Variable register 3 | 
R7 | V4 | Variable register 4 | 
R8 | V5 | Variable register 5 | 
R9 | V6 | Variable register 6 | 
R10 | V7 | Variable register 7 | 
R11 | V8 | Variable register 8 | 
R12 | IP | Intra-Procedure-call scratch register | Do not have to preserve
R13 | SP | Stack Pointer | Reserved, DO NOT USE
R14 | LR | Link Register | 
R15 | PC | Program Counter | 

## Slide 44: FUNCTION CODING CONVENTIONS Functions that modify only registers R0 - R3, R12
Using only R0-R3, R12 and no function call |  | Using only R0-R3, R12 and calling another function
f1: ● ● ● OK to modify ● R0-R3 and R12 ● BX LR |  | f2: PUSH {R3,LR} // See footnote ● ● OK to modify R0–R3, R12 ● BL f3 ● ● OK to modify R0–R3, R12 ● POP {R3,PC}
Function f3 might modify R0 – R3, R12
Adding R3 to push list preserves stack alignment.

## Slide 45: FUNCTION CODING CONVENTIONS Functions that modify for example registers R4 and R5
Using R4 and R5 and no function call |  | Using R4 and R5 and calling another function
f1: PUSH {R4,R5} ● ● OK to modify ● R0-R5 and R12 ● POP {R4,R5} BX LR |  | f2: PUSH {R3,R4,R5,LR} ● ● OK to modify ● R0–R5 and R12 ● BL f3 ● ● OK to modify ● R0–R5 and R12 ● POP {R3,R4,R5,PC}
Function f3 might modify R0-R3 and R12, but preserves R4-R11
Adding R3 to push list preserves stack alignment.

## Slide 46: FUNCTION CODING CONVENTIONS Two functions with parameters, one calling the other
C Version | Assembly Version
int32_t f1(int32_t x){ return f2(4) + x; } | f1: PUSH {R4,LR} // Preserve R4 MOV R4,R0 // Keep x safe in R4 LDR R0,=4 // R0 <-- f2’s arg BL f2 // R0 <-- f2(4) ADD R0,R0,R4 // R0 <-- f2(4) + x POP {R4,PC} // Restore R4
X is in R0, but R0 will be overwritten by f2!!!
Preserve X to R4. Of course, need to PUSH POP R4
ADD R4 and R4. And restore the original R4

## Slide 47: Done

## Slide 48: … to here …