## Slide 1: CSEN20
Fall 2025
Introduction to Embedded Systems
Michael Schimpf, PhD, mschimpf@scu.edu

## Slide 2: Chapter 8 Multiplication and Division Revisited
Part 1: Multiplication by a Constant

## Slide 3: Chapter 8 Overview
Multiplication by a Constant (w/out MUL)
  By specific constants (single instruction)
  By arbitrary constants (instruction sequence)
Division by a Constant (w/out SDIV or UDIV)
  By powers of 2 (generalization of ASR technique)
  By arbitrary constants
N % 2K: Problem using AND when N < 0
Modulus: (Different from remainder)
  Computing when divisor is a power of 2
  Computing when divisor is NOT a power of 2

## Slide 4: ARM Instruction Execution Times
Division is always slow on any processor.
Includes ADD, SUB, multiply and shifts
ARM® Corte®‑M4 Processor Technical Reference Manual, Revision r0p1.
Instructions | Clock Cycles |  | 
PUSH, POP, LDM, STM, LDRD, STRD |  |  | 1 + #regs
SDIV, UDIV |  |  | 2 - 12
Branch (B, BL, BL, B) |  |  | 2 - 4
Conditional Branch |  | Successful | 2 - 4
 |  | Failed | 1
All other LDR’s and STR’s |  |  | 2
All other instructions |  |  | 1
Some processors don’t have multiply or divide instructions, or their execution time is much greater than other instructions.
We need fast alternatives!

## Slide 5: Multiplying by Specific Constants
R0 Multiplier × R1 | Multiplier |  |  |  |  | 
ADD R0,R1,R1,LSL k |  |  |  |  |  | 
LSL R0,R1,k |  |  |  |  |  | 
RSB R0,R1,R1,LSL k |  |  |  |  |  | 
SUB R0,R1,R1,LSL k |  |  |  |  |  | 
 | Multiplier |  |  |  |  | 
ADD R0,R1,R1,LSL k |  |  |  |  |  | 
LSL R0,R1,k |  |  |  |  |  | 
RSB R0,R1,R1,LSL k |  |  |  |  |  | 
SUB R0,R1,R1,LSL k |  |  |  |  |  | 
LDR R0,=constant // to load constant into a register
MUL R0,R1,R0 //
MUL takes
2 clocks

## Slide 6: Multiplying by Arbitrary Constants
LDR R0,[] // R0 = operand
LSL R1,R0,6 // R1 = 64×
ADD R1,R1,R0,LSL 3 // R1 = 64×+ 8×
ADD R1,R1,R0,LSL 1 // R1 = 64× + 8× + 2×
LSL R1,R0,5 // R1 = 32×
SUB R1,R1,R0,LSL 1 // R1 = 32× – 2×
LSL R1,R0,1 // R1 = 2×
SUB R1,R1,R0,LSL 4 // R1 = 2× – 16×
SUB R1,R0,R0,LSL 1 // R1 = -1×
SUB R1,R1,R0,LSL 4 // R1 = -16×-1×
Multiplier | Binary Representation | Optimal Decomposition
+74 |  | 26A + 23A + 21A
+30 |  | 25A – 21A
‑14 |  | –24A + 21A
-17 |  | –24A - 20A
Multiplier | Binary Representation | Optimal Decomposition
+74 |  | 26A + 23A + 21A
+30 |  | 25A – 21A
‑14 |  | –24A + 21A
-17 |  | –24A - 20A
A span of 1’s is the same as a difference:

## Slide 7: Multiplying by Arbitrary Constants (Binary Decomposition)
1686310 = 0100 0001 1101 11112
= 214 + 28 + 27 + 26 + 24 + 23 + 22 + 21 + 20
LSL R1,R0,14 // R1 = 214R0
ADD R1,R1,R0,LSL 8 // R1 = (214 + 28)R0
ADD R1,R1,R0,LSL 7 // R1 = (214 + 28 + 27)R0
ADD R1,R1,R0,LSL 6 // R1 = (214 + 28 + 27 + 26)R0
ADD R1,R1,R0,LSL 4 // R1 = (214 + 28 + 27 + 26 + 24)R0
ADD R1,R1,R0,LSL 3 // R1 = (214 + 28 + 27 + 26 + 24 + 23)R0
ADD R1,R1,R0,LSL 2 // R1 = (214 + 28 + 27 + 26 + 24 + 23 + 22)R0
ADD R1,R1,R0,LSL 1 // R1 = (214 + 28 + 27 + 26 + 24 + 23 + 22 + 21)R0
ADD R1,R1,R0 // R1 = (214 + 28 + 27 + 26 + 24 + 23 + 22 + 21 + 20)R0
9 instructions

## Slide 8: Multiplying by Arbitrary Constants (Substring Optimization)
1686310 = 0100 0001 1101 11112
= 0100 0010 0010 0000 = 214 + 29 + 25
─ 0000 0000 0100 0001 = 26 + 20
= 214 + 29 - 26 + 25 – 20
LSL R1,R0,14 // R1 = 214R0
ADD R1,R1,R0,LSL 9 // R1 = (214 + 29)R0
SUB R1,R1,R0,LSL 6 // R1 = (214 + 29 - 26)R0
ADD R1,R1,R0,LSL 5 // R1 = (214 + 29 - 26 + 25)R0
SUB R1,R1,R0 // R1 = (214 + 29 - 26 + 25 – 20)R0
5 instructions

## Slide 9: Multiplying by Arbitrary Constants (Factoring)
1686310 = 3 7 11 73 (Prime Factors of 16863)
= 33 7 73
= 33 511
= (32 + 1) (512 – 1) = (25 + 1) (29 – 1)
ADD R1,R0,R0,LSL 5 // R1 = (25 + 1)R0
RSB R1,R1,R1,LSL 9 // R1 = (29 - 1)R1 = (29 - 1) (25 + 1)R0
2 instructions

## Slide 10: Chapter 8 Multiplication and Division Revisited
Part 2: Division by a Constant

## Slide 11: DIVIDING BY 2k (Ex: k = 3, 2k=8) With Pre-shift Adjustment
N | N/23 | N + (23-1) | (N + 23-1) ASR 3 | Decimal Result
-5 | -5/8 = 0 | +210 = 2 | 2 | 0
-13 | –13/8 = -1 | -610 = | 2 | -1
-25 | –25/8 = -3 | -1810 =2 | 2 | -3
N | N/23 | N + (23-1) | (N + 23-1) ASR 3 | Decimal Result
-5 | -5/8 = 0 |  |  | 0
-13 | –13/8 = -1 |  |  | -1
-25 | –25/8 = -3 |  |  | -3
  To divide by 2k:
  Add 2k-1 to negative dividends before the k-bit arithmetic shift right.

## Slide 12: DIVIDE BY 8 (23)
LDR R0,[] // R0 = 0????? or 1?????
ASR R1,R0,2 // R1 = 000??? or 111??
ADD R0,R0,R1,LSR 29 // R0 += (x < 0) ? 7 : 0
ASR R0,R0,3 // ÷23  Use ASR 3
STR R0,[] // y
0000000 or 0000111
÷8 = ÷23  Use LSR (32 – 3)
0
7

## Slide 13: DIVISION BY AN ARBITRARY CONSTANT Using integer multiplication to do integer division
Compute ÷ , where A and d are integers:
÷ = ×
= ( × ÷ 2N
= ( × >>
Can’t use with an integer multiply instruction!
Multiply and divide by Round the new multiplier to the nearest integer. NOTE: This is a constant to be inserted into the source code; it is NOT computed at run time.
Compute × using a double-length product. Then ( × >> is simply the most-significant half of the 2N-bit product.

## Slide 14: DIVISION BY AN ARBITRARY CONSTANT Example: Divide by 100, where is 32 bits wide
Divide 32-bit variable “x" by 100:
LDR R0,[] // R0 <-- x
LDR R1,=42949673 // 232/100 = 42949673 (Rounded)
SMULL R0,R1,R0,R1 // R1.R0 = 64-bit product
STR R1,[] // y = x/100 (approx.)
Example: x = 1534010
product = 15340 × 42949673
= 65884798382010
= 0000 0099 6666 68CC16
quotient = 0000 009916 = 15310
Rounding the multiplier to an integer sometimes introduces a small error. A more complex version of this algorithm corrects this by adjusting the dividend and/or the product as shown in the next slide.

## Slide 15: Reciprocal Multiplication
http://www.engr.scu.edu/~dlewis/book3/tools/DivideByConstant1.shtml
Appending the optional letter R rounds the result instead of truncated it by adding 0x80000000 to the 64-bit product before the most-significant half is extracted.
// Signed division by +7
LDR R0,[] // dividend
LDR R1,=2454267027
SMULL R2,R1,R1,R0
ADDS.N R1,R1,R0
LSR R0,R0,31
ADD R0,R0,R1,ASR 2
STR R0,[] // quotient
SMMLA R1,R1,R0,R0
// Signed division by +9
LDR R0,[] // dividend
LDR R1,=954437177
SMULL R2,R1,R1,R0
LSR R0,R0,31
ADD R0,R0,R1,ASR 1
STR R0,[] // quotient
SMMUL R1,R1,R0

## Slide 16: Chapter 8 Multiplication and Division Revisited
Part 3: Remainder vs. Modulus

## Slide 17: REMAINDER WHEN DIVIDING BY 2K Without using a divide instruction
For positive dividends: remainder(N, 2k) = N & (2k–1)
// remainder = N % 4 ;
LDR R0,[] // R0 = N
MOV R1,4
SDIV R2,R0,R1 // R2 = N/4
MLS R3,R2,R1,R0 // R3 = N – 4×(N/4)
STR R3,[] // remainder
// remainder = N & 3 ;
LDR R0, [] // R0 = N
AND R1,R0,3 // 310 = 00112
STR R1, [] // remainder
LDR, SDIV, MLS may take 15 clock cycles; AND takes only 1.
N10 | 0 | 1 | 2 | 3 | 4 | 5 | 6
N % 4 | 0 | 1 | 2 | 3 | 0 | 1 | 2
N2 | 0000 | 0001 | 0010 | 0011 | 0100 | 0101 | 0110
N & 0011 | 0000 | 0001 | 0010 | 0011 | 0000 | 0001 | 0010

## Slide 18: REMAINDER WHEN DIVIDING BY 2K Without using a divide instruction
For negative dividends:
If ≠ 0:
N10 | N % 4
-1 | -1
-2 | -2
-3 | -3
-4 | 0
-5 | -1
-6 | -2
N2 | (N & 3)2 | (N & 3)10 | (N & 3) - 4
1111 | 0011 | 3 | -1
1110 | 0010 | 2 | -2
1101 | 0001 | 1 | -3
1100 | 0000 | 0 | -4
1011 | 0011 | 3 | -1
1010 | 0010 | 2 | -2

## Slide 19: REMAINDER WHEN DIVIDING BY 2K Without using a divide instruction
For negative dividends:
If ≠ 0:
// int32_t Rem8(int32_t s32) ;
Rem8:
ANDS R0,R0,7 // R0 = s32 MOD 8
IT NE // Enable SUB if MOD != 0
SUBNE R0,R0,8 // Subtract 8 if MOD != 0
BX LR
NOTE: This code only works for negative dividends.
Blue hilighted text is the change needed for negative dividends.

## Slide 20: REMAINDER WHEN DIVIDING BY 2K Without using a divide instruction
For positive or negative dividends:
// int32_t Rem8(int32_t s32) ;
Rem8:
LSRS R1,R0,31 // R1 = (s32 < 0) ? 1 : 0
ANDS R0,R0,7 // R0 = s32 MOD 8
IT NE // Enable SUB if MOD != 0
SUBNE R0,R0,R1,LSL 3 // Subtract 8 if MOD != 0 && s32 < 0
BX LR
Note: Blue hilighted text is the change needed to make it
work for both positive and negative dividends.

## Slide 21: Remainder vs. Modulus
The C expression computes the remainder of divided by .
  The sign of the remainder is always that of the dividend.
However, the modulus of divided by is only defined for and is always positive and in the range to :
  Note: Remainder and MOD are different for negative operands!

## Slide 22: COMPUTING THE MODULUS
C doesn’t have a modulus operator, so how do we compute ?
If :
If ≠
If then
If ( then
N | -4 | -3 | -2 | -1
N % 3 | -1 | 0 | -2 | -1
Adjustment | Add 3 | None | Add 3 | Add 3
N mod 3 | 2 | 0 | 1 | 2
N | 0 | 1 | 2 | 3 | 4 | 5
N mod 4 | 0 | 1 | 2 | 3 | 0 | 1
N2 | 0000 | 0001 | 0010 | 0011 | 0100 | 0101
N & 3 | 0000 | 0001 | 0010 | 0011 | 0000 | 0001

## Slide 23: COMPUTING THE MODULUS When divisor
// uint32_t Modulus(int32_t dividend, int32_t divisor) ;
Modulus:
SDIV R2,R0,R1 // R2 = quotient
MLS R3,R1,R2,R0 // R3 = remainder (may be < 0)
AND R2,R1,R3,ASR 31 // R2 = (remainder < 0) ? divisor : 0
ADD R0,R3,R2 // R0 = modulus (adjusted remainder)
BX LR
  Note: “R3,ASR 31” will be all 1’s if remainder is negative, else all 0’s.
Strategy:
Calculate remainder.
If it’s negative, add the divisor.

## Slide 24: Done

## Slide 25: … to here …