## Slide 1: CSEN20
Fall 2026
Introduction to Embedded Systems
Michael Schimpf, PhD, mschimpf@scu.edu

## Slide 2: Chapter 9
Getting Started with Floating Point
Notes: The Cortex-M4 processor includes an optional FPU (or Floating Point Unit). It provides floating-point computation functionality that is compliant with the EEE 754 standard. The FPU supports all single-precision data-processing instructions and data types.

## Slide 3: Floating Point Standard (Recall)
Defined by IEEE Standard 754 -1985
Developed in response to divergence of representations
  Portability issues for scientific code
Now almost universally adopted
Two representations
  Single precision (32-bit representation)
  Double precision (64-bit representation)
https://www.h-schmidt.net/FloatConverter/IEEE754.html

## Slide 4: Floating-Point Precision
Relative precision:
  all fraction bits are significant
  Single: approx 2–23
    Equivalent to 23 × log102 ≈ 23 × 0.3 ≈ 6 decimal digits of precision
  Double: approx 2–52
    Equivalent to 52 × log102 ≈ 52 × 0.3 ≈ 16 decimal digits of precision

## Slide 5: Floating Point (recall)
Representation for non-integral numbers
  Including very small and very large numbers
Like scientific notation
  –2.3410 × 1056
  +0.00210 × 10–4
  +987.0210 × 109
In binary
  ±1.xxxxxxx2 × 2yyyy
Types in C: float (single-precision FP) and double (double-precision FP)
normalized
normalized
not normalized
Notes: For very small and very large numbers, we can not represent them in integer format. Computer arithmetic that supports such very small and very big numbers is called floating point because it represents numbers in which the binary point is not fixed (unlike the case for the integers).
In applied mathematics, a number is normalized when it is written in scientific notation with one nonzero decimal digit before the decimal point.

## Slide 6: Scientific Notation (why?)
Because calculates easier:
normalized
NOT normalized
Subscript = base
Superscript = exp
Notes: For very small and very large numbers, we can not represent them in integer format. Computer arithmetic that supports such very small and very big numbers is called floating point because it represents numbers in which the binary point is not fixed (unlike the case for the integers).
In applied mathematics, a number is normalized when it is written in scientific notation with one nonzero decimal digit before the decimal point.

## Slide 7: Floating Point
In binary
  ±1.xxxxxxx2 × 2yyyy (for example, 1.02 x 2-1=> 0.12)
Binary
point
fraction
exponent
Base 2
A tradeoff between precision and range.
Notes: Now, a designer of a floating-point representation must find a compromise between the size of the fraction (0<number<1) and the size of the exponent because a fixed word size, means you must take a bit from one to add to the other (a tradeoff between precision and range).

## Slide 8: IEEE 754 Floating-Point Format
S
Stored Exp.
Fraction
single: 8 bits
single: 23 bits
+ 127
Example: -111111.01 x 27
Notes: Like I mentioned earlier, the 754 is a technical standard for floating-point arithmetic established in 1985 by the IEEE. The 1985 version covered only binary floating-point but the current version which was published in 2019, covers all aspects of floating point arithmetic.
S: sign bit (0  non-negative, 1  negative).
Normalize significand: 1.0 ≤ |significand| < 2.0.
Always has a leading pre-binary-point 1 bit, so no need to represent it explicitly (hidden bit).
Significand is Fraction with the “1.” restored.

## Slide 9: FLOATING-POINT DATA TYPE
Exponent
Significand
31
30
23
22
0
±
Single-precision floating-point (float)
23 bits
8 bits
Precision: 23 bits ≈ 7 decimal digits
Range: 2±127 ≈ 10±38
  Our Cortex-M4 FPU doesn’t support double!
Excess-127 format
20  01111111
Normalized: MS-Bit is always 1; never stored
0 if positive,
1 if negative
Notes: The FPU of Cortex-M4F can only perform arithmetic using single-precision real numbers – identical to the C type float (does not the C type double). Although it does not support double arithmetic but the FPU registers can store doubles. One can use a pair of PFU resisters to just store a double.

## Slide 10: float versus int32_t
31 | 30 | excess 127 exponent |  |  |  |  |  | 23 | 22 | significand |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
31 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0
float x = 1000.010;
int32_t y = 100010;
9+127 =13610
111101
value2 = + 1.111101000 × 29 or (100010)
http://www.h-schmidt.net/FloatConverter/IEEE754.html
Standard Integer
float
Notes: 100010 = 111110102. = 1.111101000 x 29
Stored exponent = 127 + 9 = 136

## Slide 11: Single-precision Floating-point Representing Zero and One
S(1) Exp+127(8) (implied 0).Significand(23)
0.000 0 00000000 (0).00000000000000000000000
Implied 0, if and only if, both stored exponent and the fractional part are zero.
S(1) Exp+127(8) (implied 1).Significand(23)
0.000 0 01111111 (1).00000000000000000000000
1.00010 -> 00012 then normalize it as 1.0 x 20
Actual exponent = 0 so the stored storage in single precision becomes 0+127 = 127 or 01111111

## Slide 12: Floating-Point Example 1
Representing decimal 2.0 in IEEE 754 single-precision format:
Notes: IEEE 754 standard for single-precision floating point number..

## Slide 13: Floating-Point Example 1
Binary number 2.010 = 0000 0010.02 x 20
1. Normalize => move binary point 1 bit to the left:
1.0000 00002 x 21 (sign positive => S = 0)
2. Exponent (stored) = Actual Exponent (1) + bias
so Stored Exp. = 110 + 12710 0000 00012
    Stored Exp. = 110 + 12710 0111 11112
    Stored Exp. = 12810 1000 00002
Final bit pattern:
S(1) Exp+127(8u)(implied 1).Significand(23)
0 1000 0000 (1).0000 0000 0000 0000 0000 000
Notes: IEEE 754 standard for single-precision floating point number..

## Slide 14: Floating-Point Example 2
Representing decimal 0.75 in IEEE 754 single-precision format:
Notes: 0.750 -> 0.11 then normalize it as 1.1 x 2-1
Actual exponent = -1 so the stored storage in single precision becomes -1+127 = 126 or 01111110

## Slide 15: Floating-Point Example 2
Binary number 0.7510 = 0000 0000.112 x 20
1. Normalize => move binary point 1 bit to the right:
1.1000 00002 x 2-1 (sign positive => S = 0)
2. Exponent (stored) = Actual Exponent (1) + bias
so Stored Exp. = -110 + 12710 -0000 00012
    Stored Exp. = -110 + 12710 0111 11112
    Stored Exp. = 12610 0111 11102
Final bit pattern:
S(1) Exp+127(8u)(implied 1).Significand(23)
0 0111 1110 (1).1000 0000 0000 0000 0000 000
Notes: IEEE 754 standard for single-precision floating point number..

## Slide 16: Floating-Point Example 3
What is the binary representation of the number 63.2510 = 0011 1111.012 x 20 In the IEEE 754 single precision format?

## Slide 17: Floating-Point Example 3
Binary number 63.2510 = 0011 1111.012 x 20
1. Normalize => move binary point 5 bits to the left:
1.1111 10102 x 25 (sign positive => S = 0)
2. Exponent (stored) = Actual Exponent (1) + bias
so Stored Exp. = 510 + 12710 0000 01012
    Stored Exp. = 510 + 12710 0111 11112
    Stored Exp. = 13210 1000 01002
Final bit pattern:
S(1) Exp+127(8u)(implied 1).Significand(23)
0 1000 0100 (1).1111 1010 0000 0000 0000 000
Notes: IEEE 754 standard for single-precision floating point number..

## Slide 18: The FPU itself …

## Slide 19: FLOATING-POINT REGISTERS
32 bits
S0
S1
…
…
S14
S15
…
…
S30
S31
S16
S17
D0
D8
D7
D15
.
.
.
.
.
.
S0-S15 may be modified by functions
S16-S31 must be preserved by functions
D0-D15 may be used to hold 64-bit values, but all floating-point arithmetic is 32-bits.
Notes:   In other words, FPU has instructions for copying 64-bit values to and from the D0-D15 or to hold them temporarily, however, it can not perform any arithmetic operations on 64-bit numbers.

## Slide 20: FLOATING-POINT UNIT
Notes: So the ARM processor contains two separate computational units: The integer or the core unit and a floating-point unit. Explain the slide.
FPSCR = Floating Point Status and Control Register.
VMRS = Transfer FPU Flags to core unit APSR Flags (update nzcv flags on core unit).
Values are NOT converted between integer and floating-point representations and vice versa by just copying them from the Rs to Ss.

## Slide 21: FLOATING-POINT PUSH & POP
Instruction | Syntax | Operation
Push FPU Registers | VPUSH { register list } | SP = SP – 4 × #registers, copy registers to mem[SP]
POP FPU Registers | VPOP { register list } | Copy mem[SP] to registers SP = SP + 4 × #registers
Use these instructions at function entry and exit to preserve and restore any of the registers S16-S31 that are modified.
Notes: Instructions to push and pop FPU registers (S16 – S31).

## Slide 22: Preserving Floating-Point Registers
float foo(float f){
return bar(void) + f;
}
  Faster to preserve FPU registers in the core registers.
foo: // S0 = f
PUSH {R4,LR}
VMOV R4,S0
BL bar
VMOV S1,R4
VADD.F32 S0,S0,S1
POP {R4,PC}
foo: // S0 = f
PUSH {LR} // preserve LR
VPUSH {S16} // preserve S16
VMOV S16,S0 // keep parameter f in S16
BL bar // may modify S0-S15 (and R0-R3, R12)
VADD.F32 S0,S0,S16 // S16 = parameter f
VPOP {S16} // restore S16
POP {PC} // return (uses stack copy of LR)

## Slide 23: LOADING FLOATING-POINT CONSTANTS
  VLDR cannot be used as a pseudo-instruction.
  VMOV only works with a limited set of constants.
Integer
MOV R0,5
Floating Point
VMOV S0,3.14159
Floating Point
VMOV S0,0.5
Integer
LDR R0,=5
Floating Point
VLDR S0,=3.14159
Floating Point
LDR R0,=pi
VLDR S0,[R0]
pi: .float 3.14159
Notes: These are a few differences between instructions on the core unit versus instructions on the Floating Point unit. CLICK…
The assembler directive (.float) creates a memory location (variable) to hold an arbitrary constant such as PI. Then use VLDR to load it from that memory location/variable.

## Slide 24: VMOV Immediate Constants
The encoding of the VMOV instruction only provides 8 bits for a floating-point constant:
VMOV constants are limited to
7 | 6 |  | 4 | 3 |  |  | 0
sign |  |  |  |  |  |  | 
7 | 6 |  | 4 | 3 |  |  | 0
sign |  |  |  |  |  |  | 

## Slide 25: VMOV Immediate Constants
0.125 0.1328125 0.140625 0.1484375 0.15625 0.1640625 0.171875 0.1796875 0.1875 0.1953125 0.203125 0.2109375 0.21875 0.2265625 0.234375 0.2421875 | 0.25 0.265625 0.28125 0.296875 0.3125 0.328125 0.34375 0.359375 0.375 0.390625 0.40625 0.421875 0.4375 0.453125 0.46875 0.484375 | 0.5 0.53125 0.5625 0.59375 0.625 0.65625 0.6875 0.71875 0.75 0.78125 0.8125 0.84375 0.875 0.90625 0.9375 0.96875 | 1.0 1.0625 1.125 1.1875 1.25 1.3125 1.375 1.4375 1.5 1.5625 1.625 1.6875 1.75 1.8125 1.875 1.9375 | 2.0 2.125 2.25 2.375 2.5 2.625 2.75 2.875 3.0 3.125 3.25 3.375 3.5 3.625 3.75 3.875 | 4.0 4.25 4.5 4.75 5.0 5.25 5.5 5.75 6.0 6.25 6.5 6.75 7.0 7.25 7.5 7.75 | 8.0 8.5 9.0 9.5 10.0 10.5 11.0 11.5 12.0 12.5 13.0 13.5 14.0 14.5 15.0 15.5 | 16.0 17.0 18.0 19.0 20.0 21.0 22.0 23.0 24.0 25.0 26.0 27.0 28.0 29.0 30.0 31.0
  VMOV works for constants equal to ±m × 2-k, where 16 ≤ m ≤ 31 and 0 ≤ k ≤ 7
For m = 17 and k = 4  17 x 2-4 = 1.0625
  Visual Studio Example (VMOV)
Notes: There are only a total of 128 values that can be used by VMOV immediate instruction. These 128 values are:

## Slide 26: Common VMOV Immediates
There are a total of 128 values that can be used as VMOV immediate. The magnitudes of the most commonly used values are easily remembered as:
The first 31 multiples of : 1.0, 2.0, 3.0, 4.0, … 31.0
The first 32 multiples of : 0.5, 1.0, 1.5, 2.0, … 16.0
The first 32 multiples of : 0.25, 0.5, 0.75, 1.0, … 8.0
The first 32 multiples of : 0.125, 0.25, 0.375, … 4.0
Not supported:
VMOV S0,0.0
Use this instead:
VSUB.F32 S0,S0,S0
https://www.h-schmidt.net/FloatConverter/IEEE754.html

## Slide 27: Using Expressions to Create Constants
LDR R0,=(3*4) << 2 // this works
ADD R0,R0,5+7 // this works
VMOV S0,0.5/2.0 // syntax error!!
VMOV S0,0.25 // this works
LDR R0,=factor
VLDR S0,[R0] // S0 = (4.0/3.0)*3.14159
factor: .float (4.0/3.0)*3.14159 // syntax error!!
factor: .float 4.18879 // (4.0/3.0)*3.14159
  But you can't use expressions for floating-point constants:

## Slide 28: COPYING FLOATING-POINT DATA - Register -> Register
Instruction | Syntax | Operation
Move FP Register to FP Register | VMOV Sd,Sm | Sd = Sm
Move FP Register to Core Register | VMOV Rd,Sm | Rd = Sm
Move Core Register to FP Register | VMOV Sd,Rm | Sd = Rm
Move 2 FP Registers to Core Registers | VMOV Rt,Rt2,Sm,Sm1 | Rt = Sm ; Rt2 = Sm1 Note: m1 = m + 1
Move 2 Core Registers to FP Registers | VMOV Sm,Sm1,Rt,Rt2 | Sm = Rt ; Sm1 = Rt2 Note: m1 = m + 1
  These only copy data. They do NOT convert between integer and floating-point representations.
Notes: So please note: Moving from FP to Core register and vice versa will perform a bit by bit transfer and no conversion is performed.

## Slide 29: COPYING FLOATING-POINT DATA - Memory -> (Single or Double) Register
Instruction | Syntax | Operation
Load single-precision FPU Register from Memory | VLDR Sd,[Rn] | Sd = mem32[Rn]
 | VLDR Sd,[Rn, constant] | Sd = mem32[Rn + constant]
 | VLDR Sd,=label | Sd = mem32[addrs of label]
Load double-precision FPU Register from Memory | VLDR Dd,[Rn] | Dd = mem64[Rn]
 | VLDR Dd,[Rn, constant] | Dd = mem64[Rn + constant]
 | VLDR Dd,=label | Dd = mem64[addrs of label]
  PC-relative can only be used to reference constants stored in the read-only code space (near the instruction).
OK
Error
CPULator: 01-pi.s
Notes: Label is a variable name in memory (like x, or y).

## Slide 30: COPYING FLOATING-POINT DATA - Register -> (Single or Double) Memory
Instruction | Syntax | Operation
Store single-precision FPU Register to Memory | VSTR Sd,[Rn] | Sd = mem32[Rn]
 | VSTR Sd,[Rn,constant] | Sd = mem32[Rn + constant]
 | VSTR Sd,=label | Sd = mem32[address of label]
Store double-precision FPU Register to Memory | VSTR Dd,[Rn] | Dd = mem64[Rn]
 | VSTR Dd,[Rn,constant] | Dd = mem64[Rn + constant]
 | VSTR Dd,=label | Dd = mem64[address of label]
Notes: Does not support VSTR Sd, <variable in mem>

## Slide 31: LOADING FLOATING-POINT DATA - Memory to Multiple Registers
Instruction | Syntax | Operation
Load Multiple FPU Registers, Increment After | VLDMIA Rn!,register list | FP registers = memory, 1st address in Rn; Updates Rn only if write-back flag (!) is appended to Rn.
// Copy starting at mem[R0] VLDMIA R0!,{S0,S1,S2} (i++)
// Copy ending before mem[R0] VLDMDB R0!,{S0-S5} (++i)
Load Multiple FPU Registers, Decrement Before | VLDMDB Rn!,register list | FP registers = memory, addresses end just before address in Rn; Must append (!) and always updates Rn

## Slide 32: STORING FLOATING-POINT DATA - 1, 2 or Multiple Registers to Memory
Instruction | Syntax | Operation
Store single-precision FPU Register to Memory | VSTR Sd,[Rn] | Sd  mem32[Rn]
 | VSTR Sd,[Rn,constant] | Sd  mem32[Rn + constant]
Store double-precision FPU Register to Memory | VSTR Dd,[Rn] | Dd  mem64[Rn]
 | VSTR Dd,[Rn,constant] | Dd  mem64[Rn + constant]
Store Multiple FPU Registers, Increment After | VSTMIA Rn!,register list | FP registers  memory, 1st address in Rn; Updates Rn only if write-back flag (!) is appended to Rn.
Store Multiple FPU Registers, Decrement Before | VSTMDB Rn!,register list | FP registers  memory, addresses end just before address in Rn; Must append (!) and always updates Rn

## Slide 33: INSTRUCTION SUFFIXES
Used with VCVT* when converting between floating-point and integer values to specify the data type of the source and destination:
.F32 32-bit single-precision float
.S32 32-bit signed (2’s comp) integer
.U32 32-bit unsigned integer
The two VCVT operands must both be FPU registers (S0-S31)!
* (Floating point convert)

## Slide 34: CONVERTING BETWEEN - INTEGER AND FLOATING POINT
Instruction | Syntax | Operation
Convert Unsigned Integer to Floating-Point (float  uint32_t) | VCVT.F32.U32 Sd,Sm | Sd = (float) Sm, where Sm is an unsigned integer
Convert 2’s complement Integer to Floating-Point (float  int32_t) | VCVT.F32.S32 Sd,Sm | Sd = (float) Sm, where Sm is a signed integer
Convert Floating-Point to Unsigned Integer (uint32_t  float) | VCVT.U32.F32 Sd,Sm | Sd = (uint32_t) Sm
 | VCVTR.U32.F32 Sd,Sm | 
Convert Floating-Point to signed Integer (int32_t  float) | VCVT.S32.F32 Sd,Sm | Sd = (int32_t) Sm
 | VCVTR.S32.F32 Sd,Sm | 
  Default:
  VCVTR uses ToNEAR
  VCVT uses ToZERO
Notes: We can convert from signed and unsigned integers to floating point and vice versa.
Having the R appended to VCVT or not has to do with the rounding mode you would like to use. Next slide we are going to cover these rounding modes.

## Slide 35: ROUNDING MODES
Rounding Mode | IEEE Abbrev. | FPSCR bits 23..22 | Examples |  |  | 
 |  |  | -2.5 | -1.5 | +1.5 | +2.5
Round to nearest even (default) | ToNEAR | 00 | -2 | -2 | +2 | +2
Round towards positive infinity | ToPOSV | 01 | -2 | -1 | +2 | +3
Round towards negative infinity | ToNEGV | 10 | -3 | -2 | +1 | +2
Round towards zero (truncate) | ToZERO | 11 | -2 | -1 | +1 | +2
  Default:
  VCVTR uses ToNEAR
  VCVT uses ToZERO
0
-
+
Notes: Floating-point Status and Control Register (FPSCR)
ToZero means towards zero OR Truncate

## Slide 36: float versus int32_t POSITVE
31 | 30 | excess 127 exponent |  |  |  |  |  | 23 | 22 | significand |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
31 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0
float x = +1000.5 ; // or +(000001111101000.12)
int32_t y = +1000 ;
13610
1111010001
value2 = + 1.1111010001 × 29 or (1000.510)
VCVT.S32.F32 Sd, Sm
Sd
Sm
Notes: Here the CVT.S32.F32 Sd  (int32_t) Sm
where Sm is a float rounded towards zero (or truncate).

## Slide 37: float versus int32_t NEGATIVE
31 | 30 | excess 127 exponent |  |  |  |  |  | 23 | 22 | significand |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
31 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0
float x = -1000.5 ; // or –(000001111101000.12)
int32_t y = -1000;
13610
1111010001
value2 = - 1.1111010001 × 29 or (1000.510)
VCVT.S32.F32 Sd, Sm
Sd
Sm
Notes: Here the CVT.S32.F32 Sd  (int32_t) Sm
where Sm is a float rounded towards zero (or truncate).

## Slide 38: ARITHMETIC WITH REAL NUMBERS
Instruction | Syntax | Operation
Floating-point add | VADD.F32 Sd,Sn,Sm | Sd = Sn + Sm
Floating-point subtract | VSUB.F32 Sd,Sn,Sm | Sd = Sn − Sm
Floating-point negate | VNEG.F32 Sd,Sm | Sd = −Sm
Floating-point abs value | VABS.F32 Sd,Sm | Sd = ¦ Sm ¦ (clears FPU sign bit, N)
Floating-point multiply | VMUL.F32 Sd,Sn,Sm | Sd = Sn × Sm
Floating-point divide | VDIV.F32 Sd,Sn,Sm | Sd = Sn ÷ Sm
Floating-point square root | VSQRT.F32 Sd,Sm | Sd = (SQRT) Sm
Floating-point Multiply and Add | VMLA.F32 Sd,Sn,Sm | Sd = Sd + Sn × Sm
Floating-point Multiply and Subtract | VMLS.F32 Sd,Sn,Sm | Sd = Sd − Sn × Sm
  In general, the floating-point arithmetic instructions do not set the flags.
Notes: FPSCR (Floating Point Status and Control Register)
APSR (Application Program Status Register).

## Slide 39: FUNCTION PARAMETERS AND RETURN VALUES
Parameters:
Data of type float is passed in S0-S15
  Left-most float in S0, next float in S1, etc.
Pointer to float is passed in R0-R3
Return Value:
Result of type float is returned in S0
Result of type float * is returned in R0

## Slide 40: EXAMPLE
float foo(int, float, float *, float);
float f1, f2;
f2 = foo(5, 0.25, &f1, 1.0);
LDR R0,=5 // R0 = integer constant 5
VMOV S0,0.25 // S0 = fl-pt constant 0.25
LDR R1,=f1 // R1 = address of f1
VLDR S2,[R1]
VMOV S1,1.0 // S1 = fl-pt constant 1.0
BL foo // call function foo
LDR R0,=f2 // R0 = address of f2
VSTR S0,[R0] // store S0 in f2

## Slide 41: Algorithm Examples

## Slide 42: Another Floating-Point Example
// S0 S1 S2
float VolumeOfCube(float height, float width, float depth){
return height * width * depth;
}
VolumeOfCube: // S0 = height, S1 = width, S2 = depth
VMUL.F32 S0,S0,S1 // S0 = height * width
VMUL.F32 S0,S0,S2 // S0 = height * width * depth
BX LR
CPULator: 02-VolumOfaCube.s

## Slide 43: Special Floating-Point Constants
// S0 S1
float Discriminant(float a, float b, float c){
return b * b – 4.0 * a * c ;
}
Discriminant: // S0 = a, S1 = b, S2 = c
VMUL.F32 S1,S1,S1 // S1 = b*b
VMOV S3,#4.0 // S3 = 4.0
VMUL.F32 S3,S3,S0 // S3 = 4.0*a
VMUL.F32 S3,S3,S2 // S3 = 4.0*a*c
VSUB.F32 S0,S1,S3 // S0 = b*b – 4.0*a*c
BX LR
  VMOV works for constants equal to ±m × 2-n, where 16 ≤ m ≤ 31 and 0 ≤ n ≤ 7
CPULator: 03-Discriminant.s

## Slide 44: Arbitrary Floating-Point Constants
// S0
float AreaOfCircle(float radius){
return 3.14159 * radius * radius; }
AreaOfCircle: // S0 = radius
VMUL.F32 S0,S0,S0 // S0 = radius*radius
LDR R0,=pi // S1 = 3.14159
VLDR S1,[R0]
VMUL.F32 S0,S0,S1 // S0 = 3.14159*radius*radius
BX LR
pi: .float 3.14159
  Place data near the corresponding instruction – preferably below the function
CPULator: 04-AreaOfCircle.s

## Slide 45: Using Expressions to Create Constants
// S0
float VolumeOfSphere(float radius){
return (4.0 / 3.0) * 3.14159 * radius * radius * radius;
}
VolumeOfSphere: // S0 = radius
VMUL.F32 S1,S0,S0 // S1 = radius * radius
VMUL.F32 S0,S0,S1 // S0 = radius * radius * radius
LDR R0,=factor
VLDR S1,[R0] // S1 = (4.0/3.0)*3.14159
VMUL.F32 S0,S0,S1 // S0 = ((4.0*3.14159)/3.0)*radius^3
BX LR
factor: .float 4.18879 // (4.0/3.0)*3.14159
  You can't use expressions in the .float directive like you can with .word
CPULator: 05-VolumeOfSphere.s

## Slide 46: Preserving Floating-Point Registers
float VolumeOfCone(float radius, float height){
return AreaOfCircle(radius) * height / 3.0 ;
}
VolumeOfCone: // S0 = radius, S1 = height
PUSH {R4,LR} // Preserve R4 and LR
VMOV R4,S1 // R4 = height (S1 could be used // inside the AreaOfCircle function as // a scratch register
BL AreaOfCircle // S0 = area of base of cone
VMOV S1,R4 // S1 = height
VMUL.F32 S0,S0,S1 // S0 = height * (area of base)
VMOV S1,#3.0 // S1 = 3.0
VDIV.F32 S0,S0,S1 // S0 = (height * (area of base))/3.0
POP {R4,PC} // Restore R4 and return
  Easiest to preserve FPU registers in core registers.
S0
S1
CPULator: 06-VolumeOfCone.s
Notes: Pi * r2 * h / 3

## Slide 47: Done

## Slide 48: … to here …