## Slide 1: CSEN20
Fall 2026
Introduction to Embedded Systems
Michael Schimpf, PhD, mschimpf@scu.edu

## Slide 2: Chapter 11 Fixed-Point Reals
Part 1: Representation and Arithmetic

## Slide 3: Why Fixed-Point Reals?
Many cheap CPU chips designed for embedded applications do not have a FPU.
Software libraries that emulate a FPU can be used but are slow.
Many embedded applications are multi-threaded:
  Using a FPU significantly increases the context-switch time.
  Preserve S0 – S31

## Slide 4: What Are Fixed-Point Reals?
A way to represent a real number using an integer.
Integers imply a binary point at the far right.
    Binary point far right: 00101101.  +4510
We can imagine the binary point to be anywhere:
    Binary point midway: 0010.1101  +2.812510

## Slide 5: Q FORMAT AND THE IMAGINARY BINARY POINT
A way to specify the position of the binary point
“Q” followed by the number of bits to the right of the binary point:
Sometimes use Qm.n, where m = # integer bits and n = # fractional bits.
Integer | Q | Implied | Interpretation |  | 
+7110 (010001112) | Q0 | 01000111. | +71/20 | = | +71.0000010
 | Q3 | 01000.111 | +71/23 | = | + 8.8750010
−5610 (110010002) | Q2 | 110010.00 | −56/22 | = | −14.0000010
 | Q5 | 110.01000 | −56/25 | = | − 1.7500010
Q8.0
Q5.3
Q6.2
Q3.5

## Slide 6: ADDITION AND SUBTRACTION OF FIXED-POINT REALS
Easy as long as operands have same Q format
  Just use regular integer addition or subtraction:
Operand | Integer | Q | Interpretation |  | 
A | +3010 | Q3 | +30/23 | = | +3.75010
B | −5410 | Q3 | -54/23 | = | −6.75010
Result | Integer | Q | Interpretation |  | 
A+B | −2410 | Q3 | -24/23 | = | −3.00010
A−B | +8410 | Q3 | +84/23 | = | +10.50010
+3.750 + (-)6.750 = -3.00010
+3.750 – (-)6.750 = +10.50010
+30/8 = -3.75010
-54/8 = -6.75010

## Slide 7: ADDITION AND SUBTRACTION OF FIXED-POINT REALS
Pre-align operands with different Q formats:
Shift the operand with fewer fractional bits left:
Operand | Integer | Q | Interpretation |  | 
A | +3010 | Q3 | +30/23 | = | +3.7510
B | −5410 | Q5 | -54/25 | = | −1.687510
Result | Integer | Q | Interpretation |  | 
A+B | +6610 | Q5 | +66/25 | = | +2.062510
Operand | Integer | Q | Interpretation |  | 
A | +12010 | Q5 | +120/25 | = | +3.7510
B | −5410 | Q5 | -54/25 | = | −1.687510
* 22
Transform to Q5 format!

## Slide 8: MULTIPLICATION OF FIXED-POINT REALS
153
×23
459
306
3519
Consider what happens when you multiply two decimal reals:
1.53
×2.3
The digits of the product are determined without regard to the decimal points.
3.519
    Then the decimal point is inserted so that the number of fractional digits is the sum of those in the two operands.

## Slide 9: MULTIPLICATION OF FIXED-POINT REALS
Same as in decimal, but Q format changes
  The number of fractional bits in the product is the sum of those in the operands.
Operand | Integer | Q | Interpretation |  | 
A | +3010 | Q3 | +30/23 | = | +3.750010
B | +5110 | Q2 | +51/22 | = | +12.750010
Result | Integer | Q | Interpretation |  | 
A×B | +153010 | Q5 | +1530/25 | = | +47.812510
Add 3 + 2 = Q5

## Slide 10: DIVISION OF FIXED-POINT REALS
Consider what happens when you divide two decimal reals:
 | 971
23 | 22347
 | 207
 | 164
 | 161
 | 37
 | 23
 | 14
The digits of the quotient are determined without regard to the decimal points.
9.71
2.3 | 22.347
    Then the decimal point is inserted so that the number of fractional digits is the difference between those in the dividend less those in the divisor.

## Slide 11: DIVISION OF FIXED-POINT REALS
Integer division, but Q format changes
  The number of fractional bits in the quotient is the number in the dividend less those in the divisor
Operand | Integer | Q | Interpretation |  | 
A | +126410 | Q5 | +1264/25 | = | +39.500010
B | +8310 | Q3 | +83/23 | = | +10.375010
Result | Integer | Q | Interpretation |  | 
A÷B | +1510 | Q2 | +15/22 | = | + 3.750010 (Err: 1.50%)
SUB 5 - 3 = Q2

## Slide 12: DIVISION: IMPROVING ACCURACY
Operand | Integer | Q | Interpretation |  | 
A | +126410 | Q5 | +1264/25 | = | +39.500010
B | +8310 | Q3 | +83/23 | = | +10.375010
Result | Integer | Q | Interpretation |  | 
A÷B | +1510 | Q2 | +15/22 | = | +3.750010 (Err: 1.50%)
Shift dividend left before dividing
  Increases Q factor of dividend and thus
  Increases Q factor of quotient and thus
  Increases number of fractional digits of quotient
23×A | +1011210 | Q8 | +10112/28 | = | +39.500010
(23×A)÷B | +12110 | Q5 | +121/25 | = | + 3.7812510 (Err: 0.682%)
Increase precision * 23

## Slide 13: DIVISION: IMPROVING ACCURACY
Operand | Integer | Q | Interpretation |  | 
23×A + B/2 | +1015310 | Q8 | +10153/28 | = | +39.500010
B | +8310 | Q3 | +83/23 | = | +10.375010
Result | Integer | Q | Interpretation |  | 
(23×A+B/2)÷B | +12210 | Q5 | +122/25 | = | + 3.8125010 (Err: 0.138%)
Increase the magnitude of dividend by half that of the divisor before dividing
  Rounds the least-significant bit of quotient
  Subtract (don’t add) when dividend is negative

## Slide 14: Chapter 11 Fixed-Point Reals
Part 2: Q16.16 Format

## Slide 15: FIXED-POINT USING A UNIVERSAL Q16.16 FORMAT
Uses the same Q format for all variables
Q16.16 fits in a single 32-bit word
No pre-alignment needed to add or subtract
Product: 64 bits  32 bits x 32 bits (SMULL)
  Q16.16 result is the middle 32 bits

## Slide 16: Interpreting a Q16.16 Real
31 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 1
Implied position of Q16 binary point.
Interpret the 32-bit value as a signed 2's complement integer.
  (Implied binary point located at far right)
  0 0011 1000 1011 1100 01112 = 232,39110 (38BC716)
Move implied binary point to middle of 32-bit value.
  (Divide integer by 216 = 65,536)
  232,391 / 65,536 = 3.54610
Implied position of integer binary point.
LSR 16

## Slide 17: Converting Q16.16 to float
float Q16ToFloat(Q16 x){
return x / 65536.0; // x >> 16
}
Must be a floating-point constant
NOTE: Not using a FPU, the C run-time library provides a (slow) software emulation. Avoid using this function in any loop or repetitive computation.
  Visual Studio Example
LSR 16
LSR 16

## Slide 18: Creating a Q16.16 Real Constant
31 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
Implied position of the binary point.
typedef int32_t Q16 ; // NOTE: Container is an integer
Q16 x = 3.7 ; // NO: truncates to integer 3 (not 3.0)
Q16 x = (int32_t) (65536 * 3.7 + 0.5) ; // YES
For rounding (subtract when desired constant is negative)
Multiply by 216 so that binary point is in the middle
  Visual Studio Example
LSL 16

## Slide 19: Converting float to Q16.16
typedef int32_t Q16;
Q16 FloatToQ16(float x){
float rounding;
if (x >= 0.0)
rounding = +0.5;
else
rounding = -0.5;
return (Q16) (65536.0 * x + rounding);
}
LSL 16

## Slide 20: Converting float to Q16.16
#define ROUNDFLOAT(x) (((x) >= 0.0) ? +0.5 : -0.5)
#define FLOATTOQ16(x) (65536.0*(x) + ROUNDFLOAT(x))
When x is a constant, use a macro to avoid the computation at run-time
LSL 16

## Slide 21: Chapter 11 Fixed-Point Reals
Part 3: Q16.16 Multiplication

## Slide 22: Q16.16 × Q16.16 Multiplication
64-bit integer product
fractional part
whole part
0
63
32
31
Product (Q16.16)
Multiplier (Q16.16)
Multiplicand (Q16.16)
whole part
fractional part
31
0
32-bit integer multiplicand
whole part
fractional part
×
31
0
32-bit integer multiplier
SMULL
Some loss of range
Some loss of precision
47
16
15
48
discarded
discarded
Integer part
fractional part
NOTE: Must use signed double-length multiply since result uses part of most-significant half of the product
Integer part

## Slide 23: Q16.16 × Q16.16 Multiplication
Q16.16 variable y has 16 fractional bits
Q16.16 variable has 16 fractional bits
31 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 0
31 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 0
63 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 32 | 31 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 0
×
LDR R0,[] // R0 = x (Q16.16)
LDR R1,[] // R1 = y (Q16.16)
SMULL R0,R1,R0,R1 // R1.R0 = xy (Q32.32)
LSR R0,R0,#16 // Extract middle 32 bits
ORR R0,R0,R1,LSL#16
STR R0,[] // R0  z (Q16.16)
Thus the 64-bit Q32.32 product will have 32 fractional bits
6 instructions,
6 clock cycles
R 1
R 0

## Slide 24: Implement this example with CPUlator
Imaginary point
.
.
https://cpulator.01xz.net/?sys=arm
CPULator: 01_FixedReal_SMULL.s

## Slide 25: Implement this example with CPUlator
.
.
Imaginary point
CPULator: 01_FixedReal_SMULL.s

## Slide 26: Special Case: Multiplying Q16.16 by an Integer
Q16.16 variable has 16 fractional bits
31 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 0
31 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 0
63 |  |  |  |  |  |  | 24 | 23 |  |  |  |  |  |  | 32 | 31 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 0
×
integer N has 0 fractional bits
The 64-bit Q0.32 product will have 16 fractional bits
LDR R0,[] // R0  x (Q16.16)
LDR R1,[] // R1  N
MUL R0,R0,R1 // R0  Nx (Q16.16)
STR R0,[] // R0  y
4 instructions,
4 clock cycles

## Slide 27: Example: Q16 Area of a Triangle
Q16 AreaOfTriangle(Q16 b, Q16 h) ;
AreaOfTriangle:
SMULL R0,R1,R0,R1 // R1.R0 = Q32.32 product b x h
LSR R0,R0,#16 // Extract middle 32 bits
ORR R0,R0,R1,LSL#16
LSR R0,R0,#1 // Divide by 2
BX LR
The second LSR can be eliminated by shifting right by 17 bits instead of 16.
Example:
b = 1.5
h = 2.5
½ * 1.5 * 2.5 =1.875 = 0x1.e
CPULator: 02_FixedReal_AreaOfTriangle.s

## Slide 28: AreaOfTriangle CPUlator
CPULator: 02_FixedReal_AreaOfTriangle.s

## Slide 29: Ex: Q16 Volume of a Sphere
Q16 VolumeOfSphere(Q16 r) ;
VolumeOfSphere:
SMULL R1,R2,R0,R0 // R2.R1 = Q32.32 product r squared
LSR R1,R1,#16 // Extract Q16.16 product into R1
ORR R1,R1,R2,LSL#16
SMULL R0,R1,R1,R0 // R1.R0 = Q32.32 product r cubed
LSR R0,R0,#16 // Extract Q16.16 product into R0
ORR R0,R0,R1,LSL#16
LDR R1,=274516 // R1 = (4*pi)/3 x 65536 = 274,516.5548…
SMULL R0,R1,R0,R1 // R1.R0 = Q32.32 volume
LSR R0,R0,#16 // Extract Q16.16 product into R0
ORR R0,R0,R1,LSL#16
BX LR
Example: (4 * pi) / 3 = 4.188790205 * (1.25 * 1.25 * 1.25) = 8.181230469
1000 . 0010 1110 0110 0100
8 . 2 e 6 4
CPULator: 03_FixedReal_VolumeOfSphere.s

## Slide 30: VolumeOfSphere CPUlator
CPULator: 03_FixedReal_VolumeOfSphere.s

## Slide 31: Done

## Slide 32: … to here …