## Slide 1: CSEN20
Fall 2026
Introduction to Embedded Systems
Michael Schimpf, PhD, mschimpf@scu.edu

## Slide 2: ARM Instruction Set Architecture History

## Slide 3
Our board:
ARM Cortex-M4F: latest is M85/M52

## Slide 4: The ARMv8 Instruction Set

## Slide 5: The ARMv8 Instruction Set
ARM processors list:
Classic or Cortext-A (application): DSP, Floating Point, TrustZone, Jazelle extensions. ARMv5, ARM6 (2001)
Cortex-M (micro-controller -> mobile): ARM Thumb®-2 code density. Extended to include 32-bit instructions. First Multi-core. (2004)
Cortex-R (real time): ARMv7 Deeply pipelined micro-architecture, Flexible Multi-Processor Core (MPCore) configurations: Symmetric Multi-Processing (SMP) & Asymmetric Multi-Processing (AMP), LPAE extension.

## Slide 6: The ARMv8 Instruction Set
ARM instructions sets:
Development board/computer
  1985
  ARM1 ARMv1 (ISA)
  32-bit RISC architecture
  26-bit addressing
  16 general-purpose registers (R0–R15)
  R15 serving as the program counter (PC).
  Conditional execution for most instructions.
  No hardware multiply instruction!
  No FPU
https://en.wikipedia.org/wiki/ARM_architecture_family

## Slide 7: The ARMv8 Instruction Set
ARM instructions sets:
Acorn A3010
  1992
  ARM2 ARMv2 (ISA)
  32-bit RISC architecture
  26-bit addressing
  16 general-purpose registers (R0–R15)
  R15 serving as the program counter (PC).
  Conditional execution of instructions.
  No FPU

## Slide 8: The ARMv8 Instruction Set
New Instructions in ARMv7 (Compared to ARMv1)
MUL, MLA
SMULL, UMULL
LDRH, STRH→ Load/store doubleword (16-bit).
LDRD, STRD → Load/store doubleword (64-bit).
BX, BLX → Branch & exchange
IT → If-Then block
MSR, MRS → Move to/from system registers.
NOP → No operation
FPU & SIMD (NEON)
  VADD, VSUB, VMUL, VDIV → Vector floating-point arithmetic.
  VLDR, VSTR → Load/store floating-point registers.
  VCEQ, VCGE, VCGT → Vector comparisons.
Some others …
ARMv1

## Slide 9: ARM64 / AArch64 / ARMv8

## Slide 10: ARMv8
Instruction set:
Apple was the first to release an ARMv8-A compatible core (Cyclone) for iPhone 5S Apple A7 2013
Each instruction is 32 bit (not more, not less)
4 bit for opcode = 16 major instructions
In contrast to Intel variable instruction size
Pipeline: 4 stages for integer instructions
Pipeline: 5 stages for floating point (FP)

## Slide 11: ARMv8
Instruction set:
Apple was the first to release an ARMv8-A compatible core (Cyclone) for iPhone 5S Apple A7 2013
https://en.wikipedia.org/wiki/ARM_architecture_family

## Slide 12: ARMv8
https://en.wikipedia.org/wiki/ARM_architecture_family

## Slide 13: Registers
X0 - X30: General Purpose (64bit)
W0 - W30: General purpose (32bit)
(lower 32 bits)
SP: Stack Pointer
XZR: Zero Register (64bit)
WZR: Zero Register (32bit)
X30, LR: Link Register
PC: Program Counter

## Slide 14: ARM64
Volatile/Nonvolatile
  Registers which can be used freely are referred to as volatile
  Registers which must be preserved are referred to as non-volatile.
  Registers x0-x18 are volatile
  Registers x19-x29 are non-volatile

## Slide 15: Registers
Registers X0-X7, are volatile, because they can be changed by subroutines.
Registers X8-X17 are volatile, used for holding local variables:
  Some of these are used for special purposes by the OS and/or compiler.
Registers X19-X28, used for local variables:
  Before using them, the subroutine must preserve them.
  They are non-volatile because their contents cannot be changed by a subroutine.

## Slide 16: ARM64
General-Purpose Registers
  ARM64 provides 31 general purpose registers.
  Each register can be used as a 64-bit X-register (X0..X30)
  Or as a 32-bit W-register (W0..W30).
  Two ways of looking at the same register. W0 is the bottom 32 bits of X0:

## Slide 17: ARM64
Arithmetic Instructions:
  The choice of X or W determines the size of the operation.
  Using X registers will result in 64-bit calculations
  Using W registers will result in 32-bit calculations.
  This performs a 32-bit integer addition:
    ADD W0, W1, W2
  This performs a 64-bit integer addition:
    ADD X0, X1, X2
  All registers in an instruction must be W or X, mixing is not allowed
  When a W register is used, the top 32-bits of the 64-bit register are zeroed.

## Slide 18: ARM64
Floating-Point
  Separate set of 32 registers used for floating point and vector operations.
  These registers are 128-bit
  But they can be accessed in several ways:
    Bx is 8 bits
    Hx is 16 bits
    Sx is 32 bits
    Dx is 64 bits
    Qx is 128 bits
1-bit sign
3-bit exponent (+3 -> -3)
4-bit fractional

## Slide 19: ARM64
Other Registers
  The zero registers, XZR and WZR, always read as 0 and ignore writes.
  You can use the stack pointer (SP) as the base address for loads and stores.
  X30 is used as the Link Register and can be referred to as LR.
  The Program Counter (PC) is not a general-purpose register in A64

## Slide 20: Differences between ARMv7 and ARMv8

## Slide 21: ARM64
Overview
  Fixed length 32bit instructions
  Unaligned memory access, is now possible
    Memory is byte addressed
    Each address identifies an 8-bit byte

## Slide 22: ARM64
Traditional features
  No conditional instructions IT
  No explicit co-processors
    Everything one processor now
  No load/store multiple instructions:
    LDM
    STM
    PUSH
    POP

## Slide 23: ARM64
WAIT, no PUSH/POP?!?! 
  Broken AArch64 implementation of `push {x1}; push {x0};`
  The required stack pointer alignment is two x or four w registers
  It is not possible to push individual registers
  str x1, [sp, #-8]! // This works, but leaves `sp` with only 8-byte alignment ...
  str x0, [sp, #-8]! // ... so the second `str` will fail.
  It is wasteful – but the simplest way to handle the stack pointer to a 16-byte slot:
  str x0, [sp, #-16]! // push {x0}
  ldr x0, [sp], #16 // pop {x0}
some_func:
stp x29, x30, [sp, #-0x10]!
ldp x29, x30, [sp], #0x10
ret

## Slide 24: ARM64
Traditional features
  FPU is integrated and mandatory
  Floating-point commands are mostly the same (VADD, VMUL, …)
  Weakly ordered memory
  Integer Arithmetic basically the same

## Slide 25: ARM64
New Features
  Crypto (AES and SHA) instructions
  AdvSIMD for general purpose float math
  Larger PC-relative addressing and branching
    Conditional branches +/-1MB
    Unconditional branches +/-128MB

## Slide 26: ARM64
Conditional Instructions
  Conditional branches
    CBZ, B.cond
  Add/subtract with carry
    ADC, SBC
  Conditional compare
    CCMP
  Conditional select/set with increment, negate or invert
    CSEL, CSET (new IT block kinda)

## Slide 27: ARM64
Bit shifting
  64-bit registers (X0-X30) in addition to 32-bit (W0-W30).
  Shift amount is 6-bit (0-63 range for X registers, 0-31 for W registers).
  Explicit shift instructions exist but support both 32-bit and 64-bit values:
    LSL X0, X1, #4 // X0 = X1 << 4 (64-bit shift)
    LSR W2, W3, #1 // W2 = W3 >> 1 (32-bit shift)

## Slide 28: Operations

## Slide 29: Arithmetic Operations
Add and subtract, three operands
  Two sources and one destination
ADD w0, w1, w2 // w0 gets w1 + w2
All arithmetic operations have this form

## Slide 30: Arithmetic Example
C code: f = (g + h) - (i + j);
Compiled LEGv8 code:
ADD t0, g, h // temp t0 = g + h
ADD t1, i, j // temp t1 = i + j
SUB f, t0, t1 // f = t0 - t1

## Slide 31: Register Operand Example
C code:
f = (g + h) - (i + j);
  f, g, h, i, and j in X19, X20, X21, X22, and X23 respectively.
Compiled code:
ADD X9, X20, X21 ADD X10, X22, X23 SUB X19, X9, X10
Notes: X19 – X27: saved
X9 – X15: temporaries

## Slide 32: Immediate Operands
Constant data specified in an instruction
ADDI X22, X22, #4 // Immediate

## Slide 33: Instruction Sets
An inline barrel shifter to preprocess one of the input registers (Operand2).
Examples:
Notes: RSB R5 Operand 2 (Revers Subtract) = subtracts the value of R5 from Operand 2.
Flexible addressing of operand 2.

## Slide 34: Examples

## Slide 35: Examples
ARM64 Simulator:
http://163.238.35.161/~zhangs/arm64simulator/
Not a good simulator. Missing:
All data directives
FPU instructions
FPU registers
Registers Hex/Dec
Loading or saving examples
…
Very limited 

## Slide 36: Examples
ARM64 Simulator:
http://163.238.35.161/~zhangs/arm64simulator/

## Slide 37: Examples
1. first program: arithmetic instructions:
mov x0, #2
mov x1, #-3
add x2, x0, x1 // 2+(-3)
sub x3, x0, x1 // 2-(3)
mul x4, x0, x1 // 2*(-3)
udiv x5, x1, x0 // 2/(-3)
sdiv x6, x1, x0 // 2/(-3)

## Slide 38: Examples
2. multiply: 9*7 - 5*3
mov x1, #9 //x0 <- 9
mov x2, #7 //x1 <- 7
mul x0, x1, x2 //x0 <- x1 * x2
mov x2, #5 // x1 <- 5
mov x3, #3 // x2 <- 3
mul x1, x2, x3 // x1 <- x2 * x3
sub x0, x0, x1 // x0 <- x0 - x1

## Slide 39: Examples
3. logic instructions:
mov x0, #6
mov x1, #10
and x2, x0, x1
orr x3, x0, x1
eor x4, x0, x1

## Slide 40: Examples
4. shift instructions (show equivalence of shift to multiplication/division):
mov x0, #8
lsl x5, x0, #3 // x0*8
lsr x6, x0, #2 // x0/4
asr x7, x0, #3 // x0/8
ror x8, x0, #1

## Slide 41: Examples
5. memory access: load/store data in data segment:
first store 5 and 3 into data segment (starting address 0x800) and then load and add them together
mov x0, #5
adr x1, #0x800 //can't use mov because of 16-bit imm limit for mov
str x0, [x1]
ldr x4, [x1]
mov x0, #3
add x1, x1, #8
str x0, [x1]
ldr x5, [x1]
add x6, x4, x5
start: MOV r0,#10
ADR r4,start // SUB r4,pc,#0xc

## Slide 42: Examples
6. load/store data in stack using stack pointer sp:
mov w0, #19
str w0, [sp, #12]
ldr w0, [sp, #12]
add w0, w0, #02
add sp, sp, #0x10

## Slide 43: Examples
7. simple loop: a=0; for (i=0; i<3) a=a+2;
mov x0, #0 //a
mov x1,#0 //i
mov x2, #2
loop: add x1, x1, #1
add x0,x0,x2
cmp x1,#3
b.ne loop

## Slide 44: Examples
8. Branch instructions: if (a == 3) b=a-2; else b=a+2;
mov x0, #2
mov x1, #3 //a
cmp x1, #3
b.eq equal
add x2, x0, x1
b end
equal: sub x2, x0, x1
end:

## Slide 45: Examples
9. find the largest and put in x0
main:
mov x1, #34
mov x2, #54
mov x3, #91
mov x0, x1 // start with x1
cmp x0, x2
b.ge test_r3
mov x0, x2
test_r3:
cmp x0, x3
b.ge end
mov x0, x3
end:

## Slide 46: Examples
10. function call: main() { a=0; adder2(a);}, int adder2(int a) { return a + 2;}
main: mov w0, #0
bl adder2
ret //important, infinity loop without it
adder2: sub sp, sp, #0x10
str w0, [sp, #12]
ldr w0, [sp, #12]
add w0, w0, #0x2
add sp, sp, #0x10
ret

## Slide 47: Examples
11. computer fibonacci sequence:
main:
mov x0, 0 //answer
mov x1, 9 // find 9th number
mov x2, 0 //first number
mov x3, 1 //second number
mov x4, 0 //i=0
loop:
add x4, x4, 1
cmp x1, x4
b.le exit
mov x5, x0
add x0, x2, x3
mov x2, x0
mov x3, x5
b.al loop
exit:

## Slide 48: Done

## Slide 49: … to here …